## Slide 1
6
Physics (Triple Science) · Year 11
Chapter 6/6
Electromagnetism · AQA 8463
Transformers and the National Grid
Lessons covered
7 P15.7 Transformers (H)
8 P15.8 Transformers in action (H)
?
Big question
How can a coil of wire and a magnet turn electricity into movement, movement into electricity, and 230 V into 400 000 V?
Notes: Chapter 6 of 6: Transformers and the National Grid. How two coils on an iron core change the size of an alternating potential difference, the two transformer equations, and why the National Grid runs at hundreds of thousands of volts. (Physics only, Higher.) This deck covers the department's lessons: 7 (P15.7 Transformers (H): How does a transformer change the size of an alternating potential difference, and why does it only work with a.c.?); 8 (P15.8 Transformers in action (H): How do the transformer equations work, and why does the National Grid run at a very high potential difference?). Read the big question aloud: "How can a coil of wire and a magnet turn electricity into movement, movement into electricity, and 230 V into 400 000 V?" We come back to it at the exit ticket. Before this lesson the pre-teach group has heard the read-along and met the key words; today they lead the reading. Lesson shape: do now (recall before any help), key words, read-along, teach, then the same task three ways in (Support, Core, Stretch), exit ticket, answers. Every pupil works towards the same destination.

## Slide 2
Do now: three from memory
2
Gate
1
Choose one
Why does a transformer only work with an alternating current?
A Direct current cannot flow through an iron core
B Alternating current is stronger than direct current
C Only a changing current gives a changing magnetic field, and only a changing field induces a p.d. in the secondary coil
D The iron core only conducts electricity one way
2
Work it out
A transformer is 100 % efficient. The primary coil takes 230 V at a current of 0.5 A. The secondary coil gives 11.5 V. Calculate the current in the secondary coil in amperes.
Answer: ________ A
3
Fill the gap
In a step-up transformer the secondary coil has ___ turns than the primary coil.
Word bank: more · fewer · the same number of
Notes: Do now — retrieval. Silent, no notes, no help: recall comes before any support. Give about four minutes. 1. Why does a transformer only work with an alternating current? → C Only a changing current gives a changing magnetic field, and only a changing field induces a p.d. in the secondary coil 2. A transformer is 100 % efficient. The primary coil takes 230 V at a current of 0.5 A. The secondary coil gives 11.5 V. Calculate the current in the secondary coil in amperes. → 10 A 3. In a step-up transformer the secondary coil has ___ turns than the primary coil. → more Circulate: who gets 3/3 (Stretch route), 2/3 (Core), 0–1 (Support)? Use this to route pupils later in the lesson.

## Slide 3
Answers
2
Gate
1
Answer
C Only a changing current gives a changing magnetic field, and only a changing field induces a p.d. in the secondary coil
Why does a transformer only work with an alternating current?
Induction needs a changing field. A steady d.c. gives a steady field and induces nothing after the first instant.
2
Answer
10 A
Vp Ip = Vs Is, so Is = 230 × 0.5 ÷ 11.5 = 10 A (exact). The p.d. fell 20 times, so the current rose 20 times.
3
Answer
more
In a step-up transformer the secondary coil has ___ turns than the primary coil.
Vp / Vs = np / ns: a bigger Vs needs a bigger ns.
Notes: Answers — pupils mark their own in a different colour, then hands up for 3/3, 2/3, 1/3. 1. C Only a changing current gives a changing magnetic field, and only a changing field induces a p.d. in the secondary coil. Induction needs a changing field. A steady d.c. gives a steady field and induces nothing after the first instant. 2. 10 A. Vp Ip = Vs Is, so Is = 230 × 0.5 ÷ 11.5 = 10 A (exact). The p.d. fell 20 times, so the current rose 20 times. 3. more. Vp / Vs = np / ns: a bigger Vs needs a bigger ns. Say the route each score points to: 3/3 Stretch, 2/3 Core, 0–1 Support. Pupils may choose to move up.

## Slide 4
Key words (1 of 2)
1
Pre-teach
1
transformer
a device with two coils on an iron core that changes the size of an alternating p.d.
A phone charger has a small transformer inside it.
2
primary coil
the coil connected to the supply, which puts energy in
The mains is connected to the primary coil.
3
secondary coil
the coil that gives the output
The phone is connected to the secondary coil.
Notes: Key words. Ask the pre-teach group first: they met these words before the lesson, so they give the meaning before anyone else. For each word: say it, pupils repeat it, read the meaning, then read the example sentence together. • transformer: a device with two coils on an iron core that changes the size of an alternating p.d.. Example: "A phone charger has a small transformer inside it." • primary coil: the coil connected to the supply, which puts energy in. Example: "The mains is connected to the primary coil." • secondary coil: the coil that gives the output. Example: "The phone is connected to the secondary coil." Recall before help: cover the meanings and ask pupils to define one word from memory before moving on.

## Slide 5
Key words (2 of 2)
1
Pre-teach
4
step-up
making the potential difference bigger
A step-up transformer at the power station raises the p.d.
5
step-down
making the potential difference smaller
A step-down transformer near your home lowers the p.d. to 230 V.
6
efficient
wasting very little energy
A high p.d. makes the National Grid more efficient.
Notes: Key words. Ask the pre-teach group first: they met these words before the lesson, so they give the meaning before anyone else. For each word: say it, pupils repeat it, read the meaning, then read the example sentence together. • step-up: making the potential difference bigger. Example: "A step-up transformer at the power station raises the p.d." • step-down: making the potential difference smaller. Example: "A step-down transformer near your home lowers the p.d. to 230 V." • efficient: wasting very little energy. Example: "A high p.d. makes the National Grid more efficient." Recall before help: cover the meanings and ask pupils to define one word from memory before moving on.

## Slide 6
Read-along (1 of 2)
1
Pre-teach
Read
Read together;
pupils who were pre-taught lead
1 A transformer has two coils of wire on an iron core.
2 The primary coil is connected to an alternating supply.
3 The alternating current makes a magnetic field that keeps changing.
4 The iron core carries this changing field to the secondary coil.
5 A changing field induces an alternating potential difference in the secondary coil.
6 A steady direct current would not work, because its field does not change.
7 More turns on the secondary than the primary gives a bigger p.d.: step-up.
Notes: Read together; pupils who were pre-taught lead. The pre-teach group heard this passage (with highlighted audio in the ebook) before the lesson, so invite them to read each sentence aloud first; everyone else follows with a finger, then echo-reads it. Key words are in bold: pause on each and ask for its meaning. Sentences 1–7 of 13: 1. A transformer has two coils of wire on an iron core. 2. The primary coil is connected to an alternating supply. 3. The alternating current makes a magnetic field that keeps changing. 4. The iron core carries this changing field to the secondary coil. 5. A changing field induces an alternating potential difference in the secondary coil. 6. A steady direct current would not work, because its field does not change. 7. More turns on the secondary than the primary gives a bigger p.d.: step-up. In the ebook the audio highlights each sentence as it is read.

## Slide 7
Read-along (2 of 2)
1
Pre-teach
Read
Read together;
pupils who were pre-taught lead
8 Fewer turns on the secondary gives a smaller p.d.: step-down.
9 In a perfect transformer, the power out equals the power in.
10 So a bigger p.d. means a smaller current.
11 Power stations step the p.d. up to 400 000 V.
12 A small current wastes less energy heating the cables.
13 Near homes, the p.d. is stepped down to 230 V.
Notes: Read together; pupils who were pre-taught lead. The pre-teach group heard this passage (with highlighted audio in the ebook) before the lesson, so invite them to read each sentence aloud first; everyone else follows with a finger, then echo-reads it. Key words are in bold: pause on each and ask for its meaning. Sentences 8–13 of 13: 8. Fewer turns on the secondary gives a smaller p.d.: step-down. 9. In a perfect transformer, the power out equals the power in. 10. So a bigger p.d. means a smaller current. 11. Power stations step the p.d. up to 400 000 V. 12. A small current wastes less energy heating the cables. 13. Near homes, the p.d. is stepped down to 230 V. In the ebook the audio highlights each sentence as it is read.

## Slide 8
How a transformer works, and why it needs a.c.
Teach
!
Tip The chain for 'explain how a transformer works': alternating current in the primary → changing magnetic field in the iron core → alternating p.d. induced across the secondary.
1
A transformer is two coils of insulated wire wound on the same iron core.
2
An alternating current in the primary coil makes a magnetic field that is constantly changing in size and direction.
3
This is why a transformer only works with a.c. A steady direct current would give a steady magnetic field, and a field that is not changing induces nothing.
Notes: Teach — How a transformer works, and why it needs a.c.. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. A transformer is two coils of insulated wire wound on the same iron core. The primary coil is connected to the supply; the secondary coil is connected to whatever the transformer is powering. The two coils are not joined to each other electrically. Energy crosses from one to the other through the magnetic field. An alternating current in the primary coil makes a magnetic field that is constantly changing in size and direction. The iron core is easily magnetised and demagnetised, so it carries this changing field through the middle of the secondary coil. A changing magnetic field around a conductor induces a potential difference in it (the generator effect), so an alternating p.d. appears across the secondary coil. This is why a transformer only works with a.c. A steady direct current would give a steady magnetic field, and a field that is not changing induces nothing. The deck's slow-motion slides show it: switch a d.c. supply on and you get a single pulse in the secondary as the field builds up, and then nothing, however long you wait. Tip: The chain for 'explain how a transformer works': alternating current in the primary → changing magnetic field in the iron core → alternating p.d. induced across the secondary.

## Slide 9
Step-up, step-down, and Vp / Vs = np / ns
Teach
1
The size of the output p.d. depends on the number of turns on each coil.
2
The equation is: potential difference across the primary ÷ potential difference across the secondary = number of turns on the primary ÷ number of turns on the secondary, written Vp / Vs = np / ns.
3
To find Vs, multiply both sides out: Vs = Vp × ns ÷ np.
Notes: Teach — Step-up, step-down, and Vp / Vs = np / ns. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. The size of the output p.d. depends on the number of turns on each coil. If the secondary coil has more turns than the primary, the p.d. is stepped up: this is a step-up transformer. If the secondary has fewer turns, the p.d. is stepped down: a step-down transformer. Phone chargers, games consoles and electric toothbrushes all use step-down transformers from the 230 V mains. The equation is: potential difference across the primary ÷ potential difference across the secondary = number of turns on the primary ÷ number of turns on the secondary, written Vp / Vs = np / ns. The p.d.s are in volts; the numbers of turns have no unit. It is on the equation sheet, so your job is to rearrange it. To find Vs, multiply both sides out: Vs = Vp × ns ÷ np. To find ns: ns = np × Vs ÷ Vp. A quick sanity check saves marks: in a step-down transformer the secondary has fewer turns and a smaller p.d.; if your answer gives the secondary a bigger p.d. than the primary when it has fewer turns, something is upside down. Worked example — model it step by step, thinking aloud: A phone charger transformer has 2000 turns on its primary coil and 50 turns on its secondary. The primary is connected to the 230 V mains. Calculate the potential difference across the secondary coil. (1) Write the equation: Vp / Vs = np / ns. (2) Rearrange for Vs: Vs = Vp × ns ÷ np. (3) Substitute: Vs = 230 × 50 ÷ 2000. (4) Vs = 5.75 V. Fewer turns on the secondary, smaller p.d.: a step-down transformer, as expected. Answer: 5.75 V.

## Slide 10
Worked example: Step-up, step-down, and Vp / Vs = np / ns
Teach
A phone charger transformer has 2000 turns on its primary coil and 50 turns on its secondary. The primary is connected to the 230 V mains. Calculate the potential difference across the secondary coil.
1
Write the equation: Vp / Vs = np / ns.
2
Rearrange for Vs: Vs = Vp × ns ÷ np.
3
Substitute: Vs = 230 × 50 ÷ 2000.
4
Vs = 5.75 V. Fewer turns on the secondary, smaller p.d.: a step-down transformer, as expected.
Answer 5.75 V
Notes: Teach — Step-up, step-down, and Vp / Vs = np / ns. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. The size of the output p.d. depends on the number of turns on each coil. If the secondary coil has more turns than the primary, the p.d. is stepped up: this is a step-up transformer. If the secondary has fewer turns, the p.d. is stepped down: a step-down transformer. Phone chargers, games consoles and electric toothbrushes all use step-down transformers from the 230 V mains. The equation is: potential difference across the primary ÷ potential difference across the secondary = number of turns on the primary ÷ number of turns on the secondary, written Vp / Vs = np / ns. The p.d.s are in volts; the numbers of turns have no unit. It is on the equation sheet, so your job is to rearrange it. To find Vs, multiply both sides out: Vs = Vp × ns ÷ np. To find ns: ns = np × Vs ÷ Vp. A quick sanity check saves marks: in a step-down transformer the secondary has fewer turns and a smaller p.d.; if your answer gives the secondary a bigger p.d. than the primary when it has fewer turns, something is upside down. Worked example — model it step by step, thinking aloud: A phone charger transformer has 2000 turns on its primary coil and 50 turns on its secondary. The primary is connected to the 230 V mains. Calculate the potential difference across the secondary coil. (1) Write the equation: Vp / Vs = np / ns. (2) Rearrange for Vs: Vs = Vp × ns ÷ np. (3) Substitute: Vs = 230 × 50 ÷ 2000. (4) Vs = 5.75 V. Fewer turns on the secondary, smaller p.d.: a step-down transformer, as expected. Answer: 5.75 V.

## Slide 11
Power in, power out: Vp Ip = Vs Is
Teach
!
Tip Power is the quantity that stays the same. Work out Vp × Ip first; that number is the power, and the secondary must deliver the same power.
1
A transformer cannot create energy. In a perfect transformer, one that is 100 % efficient, the power supplied to the primary coil equals the power delivered by the secondary coil.
2
This has a consequence that surprises people. A step-up transformer increases the p.d., so to keep the power the same the current in the secondary must be smaller than in the primary.
3
Real transformers are not perfectly efficient. The coils have resistance, so a current in them heats them, and some energy is transferred to the surroundings.
Notes: Teach — Power in, power out: Vp Ip = Vs Is. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. A transformer cannot create energy. In a perfect transformer, one that is 100 % efficient, the power supplied to the primary coil equals the power delivered by the secondary coil. Electrical power is potential difference × current, so Vp × Ip = Vs × Is, with p.d. in volts, current in amperes and power in watts. This has a consequence that surprises people. A step-up transformer increases the p.d., so to keep the power the same the current in the secondary must be smaller than in the primary. A step-down transformer lowers the p.d. and raises the current. Bigger p.d. means smaller current, and the other way round. Real transformers are not perfectly efficient. The coils have resistance, so a current in them heats them, and some energy is transferred to the surroundings. Good transformers get above 95 % efficient, which is why the equation is used as if they were perfect at GCSE. Worked example — model it step by step, thinking aloud: A power-station step-up transformer takes 25 000 V at a current of 800 A on its primary side. Its output is at 400 000 V. Assuming it is 100 % efficient, calculate the current in the secondary coil. (1) Write the equation: Vp Ip = Vs Is. (2) Rearrange for Is: Is = Vp × Ip ÷ Vs. (3) Substitute: Is = 25 000 × 800 ÷ 400 000. (4) Is = 50 A. The p.d. went up 16 times, so the current came down 16 times. Answer: 50 A. Tip: Power is the quantity that stays the same. Work out Vp × Ip first; that number is the power, and the secondary must deliver the same power.

## Slide 12
Worked example: Power in, power out: Vp Ip = Vs Is
Teach
A power-station step-up transformer takes 25 000 V at a current of 800 A on its primary side. Its output is at 400 000 V. Assuming it is 100 % efficient, calculate the current in the secondary coil.
1
Write the equation: Vp Ip = Vs Is.
2
Rearrange for Is: Is = Vp × Ip ÷ Vs.
3
Substitute: Is = 25 000 × 800 ÷ 400 000.
4
Is = 50 A. The p.d. went up 16 times, so the current came down 16 times.
Answer 50 A
Notes: Teach — Power in, power out: Vp Ip = Vs Is. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. A transformer cannot create energy. In a perfect transformer, one that is 100 % efficient, the power supplied to the primary coil equals the power delivered by the secondary coil. Electrical power is potential difference × current, so Vp × Ip = Vs × Is, with p.d. in volts, current in amperes and power in watts. This has a consequence that surprises people. A step-up transformer increases the p.d., so to keep the power the same the current in the secondary must be smaller than in the primary. A step-down transformer lowers the p.d. and raises the current. Bigger p.d. means smaller current, and the other way round. Real transformers are not perfectly efficient. The coils have resistance, so a current in them heats them, and some energy is transferred to the surroundings. Good transformers get above 95 % efficient, which is why the equation is used as if they were perfect at GCSE. Worked example — model it step by step, thinking aloud: A power-station step-up transformer takes 25 000 V at a current of 800 A on its primary side. Its output is at 400 000 V. Assuming it is 100 % efficient, calculate the current in the secondary coil. (1) Write the equation: Vp Ip = Vs Is. (2) Rearrange for Is: Is = Vp × Ip ÷ Vs. (3) Substitute: Is = 25 000 × 800 ÷ 400 000. (4) Is = 50 A. The p.d. went up 16 times, so the current came down 16 times. Answer: 50 A. Tip: Power is the quantity that stays the same. Work out Vp × Ip first; that number is the power, and the secondary must deliver the same power.

## Slide 13
Why the National Grid runs at 400 000 V
Teach
!
Tip The 6-mark National Grid answer needs the chain: step-up transformer → higher p.d. → lower current for the same power → less heating of the cables → less energy wasted → more efficient; then step-down for safety at home.
1
The National Grid carries electricity from power stations to homes, offices and factories.
2
The reason is efficiency. Cables have resistance, and a current in a resistance heats it: the moving electrons collide with the ions in the metal and transfer energy to them.
3
The high p.d. is dangerous, which is why transmission cables are hung high on pylons or buried, and why they are stepped back down before they reach anything you touch.
Notes: Teach — Why the National Grid runs at 400 000 V. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. The National Grid carries electricity from power stations to homes, offices and factories. A power station's generator produces electricity at about 25 000 V. A step-up transformer raises this to about 400 000 V for the long transmission cables. Near the places that use it, step-down transformers bring it down in stages, to 230 V for homes. The reason is efficiency. Cables have resistance, and a current in a resistance heats it: the moving electrons collide with the ions in the metal and transfer energy to them. The bigger the current, the hotter the cables and the more energy is wasted to the surroundings. Power = p.d. × current, so the same power can be sent with a huge p.d. and a small current. Stepping the p.d. up reduces the current, so less energy is wasted heating the cables and the Grid is more efficient. The high p.d. is dangerous, which is why transmission cables are hung high on pylons or buried, and why they are stepped back down before they reach anything you touch. Tip: The 6-mark National Grid answer needs the chain: step-up transformer → higher p.d. → lower current for the same power → less heating of the cables → less energy wasted → more efficient; then step-down for safety at home.

## Slide 14
Same task, three ways in: Step it down (Higher)
3
Routes
1
Everyone
A step-down transformer has 920 turns on its primary coil and 40 turns on its secondary coil. The primary coil is connected to the 230 V mains. Calculate the potential difference across the secondary coil in volts.
Answer: __________ V
1
Support
1 Write Vp / Vs = np / ns.
2 Rearrange: Vs = Vp × ns ÷ np.
3 Substitute the numbers and calculate.
4 Check: fewer turns on the secondary should give a smaller p.d.
2
Core
Hint: Vs = Vp × ns ÷ np. Fewer secondary turns means a smaller answer.
3
Stretch
Then: The same transformer is 100 % efficient and the secondary delivers 2 A. Find the current in the primary coil and explain why it is smaller.
Notes: Task 1: Step it down (Higher). Same task, three ways in: one destination for everyone; only the scaffold changes. Pupils take the lane their do-now score pointed to (3/3 Stretch, 2/3 Core, 0–1 Support) and may move up at any time. Start the pre-teach group first: they know the words and the passage, so set them going on the task before you turn to the rest. Recall before help: every pupil tries from memory before opening a lane. The task: A step-down transformer has 920 turns on its primary coil and 40 turns on its secondary coil. The primary coil is connected to the 230 V mains. Calculate the potential difference across the secondary coil in volts. Support — work through the steps with the group: (1) Write Vp / Vs = np / ns. (2) Rearrange: Vs = Vp × ns ÷ np. (3) Substitute the numbers and calculate. (4) Check: fewer turns on the secondary should give a smaller p.d. Parallel worked example for Support (model it, do not give the task answer): A transformer has 460 turns on its primary and 24 turns on its secondary. The primary p.d. is 230 V. Calculate the secondary p.d. Vs = Vp × ns ÷ np.; Vs = 230 × 24 ÷ 460.; Vs = 12 V.. Answer: 12 V. Core — reveal the hint only on request: Vs = Vp × ns ÷ np. Fewer secondary turns means a smaller answer. Stretch — no help; when finished: The same transformer is 100 % efficient and the secondary delivers 2 A. Find the current in the primary coil and explain why it is smaller.

## Slide 15
Same task, three ways in: How many turns? (Higher)
3
Routes
2
Everyone
A step-up transformer at a power station has 500 turns on its primary coil, which is supplied at 25 000 V. The output across the secondary coil is 400 000 V. Calculate the number of turns on the secondary coil.
Answer: __________ turns
1
Support
1 Write Vp / Vs = np / ns.
2 Rearrange: ns = np × Vs ÷ Vp.
3 Substitute and calculate.
4 Check: step-up, so the secondary must have more turns than 500.
2
Core
Hint: ns = np × Vs ÷ Vp. The answer must be bigger than 500.
3
Stretch
Then: If this transformer is 100 % efficient and the primary current is 800 A, state the secondary current and explain why stepping up the p.d. helps the Grid.
Notes: Task 2: How many turns? (Higher). Same task, three ways in: one destination for everyone; only the scaffold changes. Pupils take the lane their do-now score pointed to (3/3 Stretch, 2/3 Core, 0–1 Support) and may move up at any time. Start the pre-teach group first: they know the words and the passage, so set them going on the task before you turn to the rest. Recall before help: every pupil tries from memory before opening a lane. The task: A step-up transformer at a power station has 500 turns on its primary coil, which is supplied at 25 000 V. The output across the secondary coil is 400 000 V. Calculate the number of turns on the secondary coil. Support — work through the steps with the group: (1) Write Vp / Vs = np / ns. (2) Rearrange: ns = np × Vs ÷ Vp. (3) Substitute and calculate. (4) Check: step-up, so the secondary must have more turns than 500. Parallel worked example for Support (model it, do not give the task answer): A transformer steps 12 V up to 240 V. Its primary has 60 turns. How many turns are on the secondary? ns = np × Vs ÷ Vp.; ns = 60 × 240 ÷ 12.; ns = 1200 turns.. Answer: 1200 turns. Core — reveal the hint only on request: ns = np × Vs ÷ Vp. The answer must be bigger than 500. Stretch — no help; when finished: If this transformer is 100 % efficient and the primary current is 800 A, state the secondary current and explain why stepping up the p.d. helps the Grid.

## Slide 16
Exit ticket
Exit
Exit
Why does a transformer only work with an alternating current?
A Alternating current is stronger than direct current
B Only a changing current gives a changing magnetic field, and only a changing field induces a p.d. in the secondary coil
C The iron core only conducts electricity one way
D Direct current cannot flow through an iron core
My answer:
Notes: Exit ticket — individual, silent, on a slip or mini-whiteboard. Recall before help: no notes, no lanes, no hints. Collect before pupils leave. Question: Why does a transformer only work with an alternating current? Answer: B Only a changing current gives a changing magnetic field, and only a changing field induces a p.d. in the secondary coil. Induction needs a changing field. A steady d.c. gives a steady field and induces nothing after the first instant. Source of this question: gate item 1 re-asked (options rotated) — this chapter has no third quick-check module. The ebook also holds task 3, "Why so high? (6 marks)", for homework or the next lesson's do now. Sort the slips: correct → ready to move on; incorrect → start next lesson in the pre-teach group, with the read-along and the Support lane. Same destination next time.

## Slide 17
Answers: Step it down (Higher)
4
Check
Answer
A step-down transformer has 920 turns on its primary coil and 40 turns on its secondary coil. The primary coil is connected to the 230 V mains. Calculate the potential difference across the secondary coil in volts.
10 V
Why
Vs = Vp × ns ÷ np = 230 × 40 ÷ 920 = 10 V. The secondary has 23 times fewer turns, so the p.d. is 23 times smaller.
Notes: Answers — task 1: Step it down (Higher). Reveal the answer; pupils mark their own work in a different colour, then read the "why" together. Same destination for every lane, so one answer serves the whole class. Answer: 10 V Why: Vs = Vp × ns ÷ np = 230 × 40 ÷ 920 = 10 V. The secondary has 23 times fewer turns, so the p.d. is 23 times smaller. Ask a Support pupil to explain one step, and a Stretch pupil to share their extension.

## Slide 18
Answers: How many turns? (Higher)
4
Check
Answer
A step-up transformer at a power station has 500 turns on its primary coil, which is supplied at 25 000 V. The output across the secondary coil is 400 000 V. Calculate the number of turns on the secondary coil.
8000 turns
Why
ns = np × Vs ÷ Vp = 500 × 400 000 ÷ 25 000 = 8000 turns. The p.d. ratio and the turns ratio are the same, 16 to 1.
Notes: Answers — task 2: How many turns? (Higher). Reveal the answer; pupils mark their own work in a different colour, then read the "why" together. Same destination for every lane, so one answer serves the whole class. Answer: 8000 turns Why: ns = np × Vs ÷ Vp = 500 × 400 000 ÷ 25 000 = 8000 turns. The p.d. ratio and the turns ratio are the same, 16 to 1. Ask a Support pupil to explain one step, and a Stretch pupil to share their extension.

## Slide 19
Answers: Exit ticket
4
Check
Answer
Why does a transformer only work with an alternating current?
B Only a changing current gives a changing magnetic field, and only a changing field induces a p.d. in the secondary coil
Why
Induction needs a changing field. A steady d.c. gives a steady field and induces nothing after the first instant.
Notes: Answers — exit ticket: Exit ticket. Reveal the answer; pupils mark their own work in a different colour, then read the "why" together. Same destination for every lane, so one answer serves the whole class. Answer: B Only a changing current gives a changing magnetic field, and only a changing field induces a p.d. in the secondary coil Why: Induction needs a changing field. A steady d.c. gives a steady field and induces nothing after the first instant. Ask a Support pupil to explain one step, and a Stretch pupil to share their extension.