## Slide 1
4
Combined Science (Physics)
Year 10 · Chapter 4/6
Electric Circuits · AQA 8464
Component characteristics: I–V graphs
Lessons covered
4 P4.4 Component characteristics
?
Big question
What decides how much current flows in each part of a circuit?
Notes: Chapter 4 of 6: Component characteristics: I–V graphs. This chapter shows how current changes with potential difference for a resistor, a filament lamp, a diode, a thermistor and an LDR. This deck covers the department's lesson: 4 (P4.4 Component characteristics: How does the current through different components change as the potential difference changes?). Read the big question aloud: "What decides how much current flows in each part of a circuit?" We come back to it at the exit ticket. Before this lesson the pre-teach group has heard the read-along and met the key words; today they lead the reading. Lesson shape: do now (recall before any help), key words, read-along, teach, then the same task three ways in (Support, Core, Stretch), exit ticket, answers. Every pupil works towards the same destination.

## Slide 2
Do now: three from memory
2
Gate
1
Choose one
Which component has an I–V graph that is a straight line through the origin?
A an LDR as the light changes
B a diode
C a filament lamp
D a resistor at constant temperature
2
Fill the gap
As the temperature of a thermistor increases, its resistance ___.
Word bank: increases · decreases · stays the same
3
Work it out
The p.d. across a resistor is 4.0 V and the current is 0.50 A. Calculate its resistance in ohms.
Answer: ________ Ω
Notes: Do now — retrieval. Silent, no notes, no help: recall comes before any support. Give about four minutes. 1. Which component has an I–V graph that is a straight line through the origin? → D a resistor at constant temperature 2. As the temperature of a thermistor increases, its resistance ___. → decreases 3. The p.d. across a resistor is 4.0 V and the current is 0.50 A. Calculate its resistance in ohms. → 8 Ω Circulate: who gets 3/3 (Stretch route), 2/3 (Core), 0–1 (Support)? Use this to route pupils later in the lesson.

## Slide 3
Answers
2
Gate
1
Answer
D a resistor at constant temperature
Which component has an I–V graph that is a straight line through the origin?
A resistor at constant temperature is ohmic: current is directly proportional to p.d., giving a straight line through the origin.
2
Answer
decreases
As the temperature of a thermistor increases, its resistance ___.
A thermistor's resistance decreases as its temperature increases.
3
Answer
8 Ω
The p.d. across a resistor is 4.0 V and the current is 0.50 A. Calculate its resistance in ohms.
R = V ÷ I = 4.0 ÷ 0.50 = 8.0 Ω (2 s.f.).
Notes: Answers — pupils mark their own in a different colour, then hands up for 3/3, 2/3, 1/3. 1. D a resistor at constant temperature. A resistor at constant temperature is ohmic: current is directly proportional to p.d., giving a straight line through the origin. 2. decreases. A thermistor's resistance decreases as its temperature increases. 3. 8 Ω. R = V ÷ I = 4.0 ÷ 0.50 = 8.0 Ω (2 s.f.). Say the route each score points to: 3/3 Stretch, 2/3 Core, 0–1 Support. Pupils may choose to move up.

## Slide 4
Key words (1 of 2)
1
Pre-teach
1
graph
a picture of how one measurement changes with another
We drew a graph of current against potential difference.
2
directly proportional
when one thing doubles, the other doubles too
For the resistor, the current was directly proportional to the p.d.
3
filament
the thin coil of wire inside a lamp that glows when hot
The filament gets very hot when current flows through it.
Notes: Key words. Ask the pre-teach group first: they met these words before the lesson, so they give the meaning before anyone else. For each word: say it, pupils repeat it, read the meaning, then read the example sentence together. • graph: a picture of how one measurement changes with another. Example: "We drew a graph of current against potential difference." • directly proportional: when one thing doubles, the other doubles too. Example: "For the resistor, the current was directly proportional to the p.d." • filament: the thin coil of wire inside a lamp that glows when hot. Example: "The filament gets very hot when current flows through it." Recall before help: cover the meanings and ask pupils to define one word from memory before moving on.

## Slide 5
Key words (2 of 2)
1
Pre-teach
4
thermistor
a resistor that changes with temperature
When the thermistor warmed up, its resistance went down.
5
LDR
a light dependent resistor, which changes with light
In bright light the LDR had a low resistance.
Notes: Key words. Ask the pre-teach group first: they met these words before the lesson, so they give the meaning before anyone else. For each word: say it, pupils repeat it, read the meaning, then read the example sentence together. • thermistor: a resistor that changes with temperature. Example: "When the thermistor warmed up, its resistance went down." • LDR: a light dependent resistor, which changes with light. Example: "In bright light the LDR had a low resistance." Recall before help: cover the meanings and ask pupils to define one word from memory before moving on.

## Slide 6
Read-along
1
Pre-teach
Read
Read together;
pupils who were pre-taught lead
1 Different components behave in different ways.
2 To see how, we change the p.d. and measure the current.
3 Then we draw a graph of current against p.d.
4 For a resistor, the graph is a straight line through zero.
5 This means the current is directly proportional to the p.d.
6 For a filament lamp, the graph is a curve.
7 The filament gets hot, and its resistance goes up.
8 A diode only lets current flow one way.
9 A thermistor has less resistance when it is warm.
10 An LDR has less resistance when the light is bright.
11 These components help machines react to heat and light.
Notes: Read together; pupils who were pre-taught lead. The pre-teach group heard this passage (with highlighted audio in the ebook) before the lesson, so invite them to read each sentence aloud first; everyone else follows with a finger, then echo-reads it. Key words are in bold: pause on each and ask for its meaning. Sentences 1–11 of 11: 1. Different components behave in different ways. 2. To see how, we change the p.d. and measure the current. 3. Then we draw a graph of current against p.d. 4. For a resistor, the graph is a straight line through zero. 5. This means the current is directly proportional to the p.d. 6. For a filament lamp, the graph is a curve. 7. The filament gets hot, and its resistance goes up. 8. A diode only lets current flow one way. 9. A thermistor has less resistance when it is warm. 10. An LDR has less resistance when the light is bright. 11. These components help machines react to heat and light. In the ebook the audio highlights each sentence as it is read.

## Slide 7
Testing a component and reading an I–V graph
Teach
!
Tip I–V graph: steeper line = lower resistance.
Worked example
On a resistor's I–V graph, the line passes through 1.5 V and 0.10 A. Calculate the resistance.
1
Read the point: V = 1.5 V, I = 0.10 A.
2
Use R = V ÷ I.
3
R = 1.5 ÷ 0.10 = 15 Ω.
Answer 15 Ω
To test a component, connect it in series with a cell or power supply, a variable resistor and an ammeter, with a voltmeter across the component.
Plot current (I) up the side and potential difference (V) along the bottom: this is an I–V graph.
On an I–V graph, a steeper line means more current for each volt, which means a lower resistance.
Notes: Teach — Testing a component and reading an I–V graph. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. To test a component, connect it in series with a cell or power supply, a variable resistor and an ammeter, with a voltmeter across the component. Change the variable resistor to get different currents, and record the p.d. and current each time. Then reverse the supply connections and repeat to get negative values. Plot current (I) up the side and potential difference (V) along the bottom: this is an I–V graph. For a resistor at constant temperature, the points lie on a straight line through the origin. The current is directly proportional to the p.d., so its resistance is constant: it is an ohmic conductor. On an I–V graph, a steeper line means more current for each volt, which means a lower resistance. To find the resistance at any point, read off V and I and use R = V ÷ I. This is required practical work: you must be able to do it for a resistor, a filament lamp and a diode. Worked example — model it step by step, thinking aloud: On a resistor's I–V graph, the line passes through 1.5 V and 0.10 A. Calculate the resistance. (1) Read the point: V = 1.5 V, I = 0.10 A. (2) Use R = V ÷ I. (3) R = 1.5 ÷ 0.10 = 15 Ω. Answer: 15 Ω. Tip: I–V graph: steeper line = lower resistance.

## Slide 8
The filament lamp and the diode
Teach
!
Tip Hotter metal = ions vibrate more = more collisions = more resistance.
Worked example
A filament lamp takes 0.20 A at 1.0 V and 0.30 A at 3.0 V. Show that its resistance increases.
1
At 1.0 V: R = V ÷ I = 1.0 ÷ 0.20 = 5.0 Ω.
2
At 3.0 V: R = V ÷ I = 3.0 ÷ 0.30 = 10 Ω.
3
The resistance has doubled, from 5.0 Ω to 10 Ω, as the filament got hotter.
Answer 5.0 Ω at 1.0 V, rising to 10 Ω at 3.0 V
A filament lamp's I–V graph starts steep and then curves over, getting flatter as the p.d. increases.
A diode has a very high resistance in the reverse direction, so almost no current flows.
So for a lamp you work out the resistance at each point with R = V ÷ I, and you find it grows as V grows.
Notes: Teach — The filament lamp and the diode. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. A filament lamp's I–V graph starts steep and then curves over, getting flatter as the p.d. increases. The shape is the same, upside down, for negative values. As the current increases, the filament gets hotter. The metal ions vibrate more, the electrons collide with them more often, and so the resistance increases. A filament lamp is not ohmic. A diode has a very high resistance in the reverse direction, so almost no current flows. In the forward direction, almost no current flows until the p.d. reaches a small value (for a typical silicon diode, about 0.6 to 0.7 V); after that the current rises steeply, because the resistance becomes low. So for a lamp you work out the resistance at each point with R = V ÷ I, and you find it grows as V grows. Worked example — model it step by step, thinking aloud: A filament lamp takes 0.20 A at 1.0 V and 0.30 A at 3.0 V. Show that its resistance increases. (1) At 1.0 V: R = V ÷ I = 1.0 ÷ 0.20 = 5.0 Ω. (2) At 3.0 V: R = V ÷ I = 3.0 ÷ 0.30 = 10 Ω. (3) The resistance has doubled, from 5.0 Ω to 10 Ω, as the filament got hotter. Answer: 5.0 Ω at 1.0 V, rising to 10 Ω at 3.0 V. Tip: Hotter metal = ions vibrate more = more collisions = more resistance.

## Slide 9
Thermistors and LDRs: sensing components
Teach
!
Tip Thermistor: hotter, lower R. LDR: brighter, lower R.
Worked example
An LDR has 6.0 V across it. In the dark the current is 0.0012 A; in bright light it is 0.060 A. Calculate its resistance in the dark.
1
Use R = V ÷ I.
2
In the dark: R = 6.0 ÷ 0.0012 = 5000 Ω.
3
In bright light: R = 6.0 ÷ 0.060 = 100 Ω, so the resistance falls as the light gets brighter.
Answer 5000 Ω in the dark (100 Ω in bright light)
The resistance of a thermistor decreases as its temperature increases.
The resistance of a light dependent resistor (LDR) decreases as the light falling on it gets brighter.
Because their resistance changes so much, these components let a circuit react to its surroundings.
Notes: Teach — Thermistors and LDRs: sensing components. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. The resistance of a thermistor decreases as its temperature increases. Thermostats in fridges, ovens and heating systems use thermistors to sense temperature and switch things on or off. The resistance of a light dependent resistor (LDR) decreases as the light falling on it gets brighter. Security lights and street lights use LDRs to switch on when it gets dark, because in the dark the LDR's resistance becomes high. Because their resistance changes so much, these components let a circuit react to its surroundings. You calculate their resistance in exactly the same way, with R = V ÷ I. Worked example — model it step by step, thinking aloud: An LDR has 6.0 V across it. In the dark the current is 0.0012 A; in bright light it is 0.060 A. Calculate its resistance in the dark. (1) Use R = V ÷ I. (2) In the dark: R = 6.0 ÷ 0.0012 = 5000 Ω. (3) In bright light: R = 6.0 ÷ 0.060 = 100 Ω, so the resistance falls as the light gets brighter. Answer: 5000 Ω in the dark (100 Ω in bright light). Tip: Thermistor: hotter, lower R. LDR: brighter, lower R.

## Slide 10
The task: Match the component to its behaviour
4
Same task
1
Match each component to its behaviour.
1
resistor at constant temperature
A
straight-line I–V graph through the origin
2
filament lamp
B
resistance decreases as light gets brighter
3
diode
C
resistance decreases as temperature increases
4
thermistor
D
I–V graph curves over, getting flatter as the p.d. increases
5
LDR
E
current flows in one direction only
Notes: Task 1: Match the component to its behaviour. Same task, three ways in: one destination for everyone; only the scaffold changes. Pupils take the lane their do-now score pointed to (3/3 Stretch, 2/3 Core, 0–1 Support) and may move up at any time. Start the pre-teach group first: they know the words and the passage, so set them going on the task before you turn to the rest. Recall before help: every pupil tries from memory before opening a lane. The task: Match each component to its behaviour. Support — work through the steps with the group: (1) Start with the one you are surest of: the diode is the one-way component. (2) The two sensors are named for what they sense: thermistor (thermal = heat), LDR (light). (3) Of the two graphs left, the resistor is the straight one and the lamp is the curve. Parallel worked example for Support (model it, do not give the task answer): Match each I–V graph feature to its meaning: a steep straight line; a shallow straight line; a flat line along the V axis. Steep line: a lot of current per volt = low resistance.; Shallow line: little current per volt = high resistance.; Flat line: no current at all = very high resistance.. Answer: low resistance; high resistance; very high resistance. Core — reveal the hint only on request: Two of these are sensors; one is a one-way valve; one gets hot. Stretch — no help; when finished: Sketch the I–V graph for a diode, including negative p.d. values, and label where its resistance is high and where it is low.

## Slide 11
Same task, three ways in: Match the component to its behaviour
3
Routes
1
Everyone
Match each component to its behaviour.
1
Support
1 Start with the one you are surest of: the diode is the one-way component.
2 The two sensors are named for what they sense: thermistor (thermal = heat), LDR (light).
3 Of the two graphs left, the resistor is the straight one and the lamp is the curve.
2
Core
Hint: Two of these are sensors; one is a one-way valve; one gets hot.
3
Stretch
Then: Sketch the I–V graph for a diode, including negative p.d. values, and label where its resistance is high and where it is low.
Notes: Task 1: Match the component to its behaviour. Same task, three ways in: one destination for everyone; only the scaffold changes. Pupils take the lane their do-now score pointed to (3/3 Stretch, 2/3 Core, 0–1 Support) and may move up at any time. Start the pre-teach group first: they know the words and the passage, so set them going on the task before you turn to the rest. Recall before help: every pupil tries from memory before opening a lane. The task: Match each component to its behaviour. Support — work through the steps with the group: (1) Start with the one you are surest of: the diode is the one-way component. (2) The two sensors are named for what they sense: thermistor (thermal = heat), LDR (light). (3) Of the two graphs left, the resistor is the straight one and the lamp is the curve. Parallel worked example for Support (model it, do not give the task answer): Match each I–V graph feature to its meaning: a steep straight line; a shallow straight line; a flat line along the V axis. Steep line: a lot of current per volt = low resistance.; Shallow line: little current per volt = high resistance.; Flat line: no current at all = very high resistance.. Answer: low resistance; high resistance; very high resistance. Core — reveal the hint only on request: Two of these are sensors; one is a one-way valve; one gets hot. Stretch — no help; when finished: Sketch the I–V graph for a diode, including negative p.d. values, and label where its resistance is high and where it is low.

## Slide 12
Same task, three ways in: Why does a lamp's resistance rise?
3
Routes
2
Everyone
Explain why the resistance of a filament lamp increases as the potential difference across it increases.
4 marks · Write in full sentences
1
Support
1 Link p.d. to current: more push, more current.
2 Link current to temperature: the filament heats up.
3 Link temperature to ions and collisions, then to resistance.
2
Core
Hint: Use a chain: p.d., current, temperature, ions, collisions, resistance.
3
Stretch
Then: Explain why a filament lamp is called non-ohmic, and why a resistor kept in cold water during an experiment behaves differently.
Notes: Task 2: Why does a lamp's resistance rise?. Same task, three ways in: one destination for everyone; only the scaffold changes. Pupils take the lane their do-now score pointed to (3/3 Stretch, 2/3 Core, 0–1 Support) and may move up at any time. Start the pre-teach group first: they know the words and the passage, so set them going on the task before you turn to the rest. Recall before help: every pupil tries from memory before opening a lane. The task: Explain why the resistance of a filament lamp increases as the potential difference across it increases. Support — work through the steps with the group: (1) Link p.d. to current: more push, more current. (2) Link current to temperature: the filament heats up. (3) Link temperature to ions and collisions, then to resistance. Parallel worked example for Support (model it, do not give the task answer): Explain why a long wire has a greater resistance than a short wire of the same metal. Electrons must travel past more metal ions in a long wire.; So they make more collisions on the way.; More collisions mean more resistance.. Answer: A longer wire means more ions to collide with, so more collisions and more resistance.. Core — reveal the hint only on request: Use a chain: p.d., current, temperature, ions, collisions, resistance. Stretch — no help; when finished: Explain why a filament lamp is called non-ohmic, and why a resistor kept in cold water during an experiment behaves differently.

## Slide 13
Exit ticket
Exit
Exit
On a filament lamp's I–V graph, the current is 0.40 A when the p.d. is 6.0 V. Calculate the resistance of the lamp at this point, in ohms.
My answer (Ω):
Notes: Exit ticket — individual, silent, on a slip or mini-whiteboard. Recall before help: no notes, no lanes, no hints. Collect before pupils leave. Question: On a filament lamp's I–V graph, the current is 0.40 A when the p.d. is 6.0 V. Calculate the resistance of the lamp at this point, in ohms. Answer: 15 Ω. R = V ÷ I = 6.0 ÷ 0.40 = 15 Ω. It is higher than at lower p.d. because the filament is hotter. Source of this question: module 3 task ("Resistance from a graph reading") from the manifest. Sort the slips: correct → ready to move on; incorrect → start next lesson in the pre-teach group, with the read-along and the Support lane. Same destination next time.

## Slide 14
Answers: Match the component to its behaviour
4
Check
Answer
1 resistor at constant temperature → A straight-line I–V graph through the origin
2 filament lamp → D I–V graph curves over, getting flatter as the p.d. increases
3 diode → E current flows in one direction only
4 thermistor → C resistance decreases as temperature increases
5 LDR → B resistance decreases as light gets brighter
Why
An ohmic resistor gives a straight line; filament lamp = curve as it heats; diode = one way; thermistor = falls with heat; LDR = falls with light.
Notes: Answers — task 1: Match the component to its behaviour. Reveal the answer; pupils mark their own work in a different colour, then read the "why" together. Same destination for every lane, so one answer serves the whole class. Answer: resistor at constant temperature → A straight-line I–V graph through the origin; filament lamp → D I–V graph curves over, getting flatter as the p.d. increases; diode → E current flows in one direction only; thermistor → C resistance decreases as temperature increases; LDR → B resistance decreases as light gets brighter Why: An ohmic resistor gives a straight line; filament lamp = curve as it heats; diode = one way; thermistor = falls with heat; LDR = falls with light. Ask a Support pupil to explain one step, and a Stretch pupil to share their extension.

## Slide 15
Answers: Why does a lamp's resistance rise?
4
Check
Success criteria: tick what you did
A bigger p.d. gives a bigger current through the filament.
The filament gets hotter.
The metal ions vibrate more.
Electrons collide with the ions more often, so the resistance increases.
Model answer
As the potential difference increases, the current through the filament increases, so more energy is transferred to it and it gets hotter. In a hotter metal the ions vibrate more, so the electrons flowing through collide with them more often. More collisions mean the filament opposes the current more, so its resistance increases.
Notes: Answers — task 2: Why does a lamp's resistance rise?. Reveal the answer; pupils mark their own work in a different colour, then read the "why" together. Same destination for every lane, so one answer serves the whole class. Answer: A bigger p.d. gives a bigger current through the filament.; The filament gets hotter.; The metal ions vibrate more.; Electrons collide with the ions more often, so the resistance increases. Why: The four links are current rising, the filament heating, ions vibrating more and electrons colliding more often. Model answer: As the potential difference increases, the current through the filament increases, so more energy is transferred to it and it gets hotter. In a hotter metal the ions vibrate more, so the electrons flowing through collide with them more often. More collisions mean the filament opposes the current more, so its resistance increases. Success criteria: A bigger p.d. gives a bigger current through the filament.; The filament gets hotter.; The metal ions vibrate more.; Electrons collide with the ions more often, so the resistance increases. Ask a Support pupil to explain one step, and a Stretch pupil to share their extension.

## Slide 16
Answers: Exit ticket
4
Check
Answer
On a filament lamp's I–V graph, the current is 0.40 A when the p.d. is 6.0 V. Calculate the resistance of the lamp at this point, in ohms.
15 Ω
Why
R = V ÷ I = 6.0 ÷ 0.40 = 15 Ω. It is higher than at lower p.d. because the filament is hotter.
Notes: Answers — exit ticket: Exit ticket. Reveal the answer; pupils mark their own work in a different colour, then read the "why" together. Same destination for every lane, so one answer serves the whole class. Answer: 15 Ω Why: R = V ÷ I = 6.0 ÷ 0.40 = 15 Ω. It is higher than at lower p.d. because the filament is hotter. Ask a Support pupil to explain one step, and a Stretch pupil to share their extension.