## Slide 1
6
Combined Science (Physics)
Year 10 · Chapter 6/6
Electric Circuits · AQA 8464
Parallel circuits
Lessons covered
6 P4.6 Parallel circuits
?
Big question
What decides how much current flows in each part of a circuit?
Notes: Chapter 6 of 6: Parallel circuits. This chapter gives you the rules for a parallel circuit, and shows why your home is wired in parallel. This deck covers the department's lesson: 6 (P4.6 Parallel circuits: What are the rules for current and potential difference in a parallel circuit?). Read the big question aloud: "What decides how much current flows in each part of a circuit?" We come back to it at the exit ticket. Before this lesson the pre-teach group has heard the read-along and met the key words; today they lead the reading. Lesson shape: do now (recall before any help), key words, read-along, teach, then the same task three ways in (Support, Core, Stretch), exit ticket, answers. Every pupil works towards the same destination.

## Slide 2
Do now: three from memory
2
Gate
1
Fill the gap
In a parallel circuit, the p.d. across each branch is ___ the supply p.d.
Word bank: the same as · less than · more than
2
Choose one
Two branches of a parallel circuit carry 0.40 A and 0.60 A. What is the current from the supply?
A 1.0 A
B 0.24 A
C 0.50 A
D 0.20 A
3
Work it out
The supply current in a parallel circuit is 2.5 A. One branch carries 1.5 A. Calculate the current in the other branch, in amps.
Answer: ________ A
Notes: Do now — retrieval. Silent, no notes, no help: recall comes before any support. Give about four minutes. 1. In a parallel circuit, the p.d. across each branch is ___ the supply p.d. → the same as 2. Two branches of a parallel circuit carry 0.40 A and 0.60 A. What is the current from the supply? → A 1.0 A 3. The supply current in a parallel circuit is 2.5 A. One branch carries 1.5 A. Calculate the current in the other branch, in amps. → 1 A Circulate: who gets 3/3 (Stretch route), 2/3 (Core), 0–1 (Support)? Use this to route pupils later in the lesson.

## Slide 3
Answers
2
Gate
1
Answer
the same as
In a parallel circuit, the p.d. across each branch is ___ the supply p.d.
Each branch is connected straight across the supply, so it has the full supply p.d.
2
Answer
A 1.0 A
Two branches of a parallel circuit carry 0.40 A and 0.60 A. What is the current from the supply?
The branch currents add up: 0.40 + 0.60 = 1.0 A.
3
Answer
1 A
The supply current in a parallel circuit is 2.5 A. One branch carries 1.5 A. Calculate the current in the other branch, in amps.
The branch currents add up to the supply current: 2.5 − 1.5 = 1.0 A (2 s.f.).
Notes: Answers — pupils mark their own in a different colour, then hands up for 3/3, 2/3, 1/3. 1. the same as. Each branch is connected straight across the supply, so it has the full supply p.d. 2. A 1.0 A. The branch currents add up: 0.40 + 0.60 = 1.0 A. 3. 1 A. The branch currents add up to the supply current: 2.5 − 1.5 = 1.0 A (2 s.f.). Say the route each score points to: 3/3 Stretch, 2/3 Core, 0–1 Support. Pupils may choose to move up.

## Slide 4
Key words
1
Pre-teach
Word
What it means
In a sentence
parallel
joined on separate branches, side by side
The two lamps were joined in parallel, each on its own branch.
branch
one of the separate paths in a parallel circuit
Each branch had one lamp in it.
junction
a point where wires split apart or join together
At the junction the current split into two.
split
divide into parts
The current splits between the branches and joins up again.
Notes: Key words. Ask the pre-teach group first: they met these words before the lesson, so they give the meaning before anyone else. For each word: say it, pupils repeat it, read the meaning, then read the example sentence together. • parallel: joined on separate branches, side by side. Example: "The two lamps were joined in parallel, each on its own branch." • branch: one of the separate paths in a parallel circuit. Example: "Each branch had one lamp in it." • junction: a point where wires split apart or join together. Example: "At the junction the current split into two." • split: divide into parts. Example: "The current splits between the branches and joins up again." Recall before help: cover the meanings and ask pupils to define one word from memory before moving on.

## Slide 5
Read-along
1
Pre-teach
Read
Read together;
pupils who were pre-taught lead
1 A parallel circuit has more than one loop.
2 Each loop is called a branch.
3 At a junction, the current splits between the branches.
4 Later, the branches join and the current adds up again.
5 It is like a river flowing round both sides of an island.
6 Each branch gets the full p.d. of the supply.
7 If one lamp breaks, the other branches still work.
8 Adding another branch gives the current another path.
9 So the total current from the supply goes up.
10 The houses we live in are wired in parallel.
Notes: Read together; pupils who were pre-taught lead. The pre-teach group heard this passage (with highlighted audio in the ebook) before the lesson, so invite them to read each sentence aloud first; everyone else follows with a finger, then echo-reads it. Key words are in bold: pause on each and ask for its meaning. Sentences 1–10 of 10: 1. A parallel circuit has more than one loop. 2. Each loop is called a branch. 3. At a junction, the current splits between the branches. 4. Later, the branches join and the current adds up again. 5. It is like a river flowing round both sides of an island. 6. Each branch gets the full p.d. of the supply. 7. If one lamp breaks, the other branches still work. 8. Adding another branch gives the current another path. 9. So the total current from the supply goes up. 10. The houses we live in are wired in parallel. In the ebook the audio highlights each sentence as it is read.

## Slide 6
Branches and potential difference
Teach
!
Tip Parallel: every branch gets the full supply p.d.
Worked example
A 6.0 V battery is connected to a 12 Ω lamp on its own branch. Calculate the current in that branch.
1
The branch has the full supply p.d. across it: V = 6.0 V.
2
Use I = V ÷ R.
3
I = 6.0 ÷ 12 = 0.50 A.
Answer 0.50 A
A parallel circuit has more than one loop, or branch.
This means each branch works on its own. You can find the current in any branch with I = V ÷ R, using the supply p.d. and the resistance of that branch.
Notes: Teach — Branches and potential difference. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. A parallel circuit has more than one loop, or branch. Each branch is connected straight across the supply, so the p.d. across each branch is the same as the supply p.d.: V(supply) = V₁ = V₂. This means each branch works on its own. You can find the current in any branch with I = V ÷ R, using the supply p.d. and the resistance of that branch. Worked example — model it step by step, thinking aloud: A 6.0 V battery is connected to a 12 Ω lamp on its own branch. Calculate the current in that branch. (1) The branch has the full supply p.d. across it: V = 6.0 V. (2) Use I = V ÷ R. (3) I = 6.0 ÷ 12 = 0.50 A. Answer: 0.50 A. Tip: Parallel: every branch gets the full supply p.d.

## Slide 7
Current splits and rejoins
Teach
!
Tip The branch currents add up to the current from the supply.
1
Think of a river flowing round an island. The water splits between the two channels and joins up again downstream: the water in the two channels adds up to the water in the river.
2
The total current from the supply is the sum of the currents in the separate branches: I(total) = I₁ + I₂ + ….
Notes: Teach — Current splits and rejoins. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. Think of a river flowing round an island. The water splits between the two channels and joins up again downstream: the water in the two channels adds up to the water in the river. Current behaves the same way at a junction. The total current from the supply is the sum of the currents in the separate branches: I(total) = I₁ + I₂ + …. A branch with a lower resistance takes a bigger share of the current. Worked example — model it step by step, thinking aloud: A 12 V supply is connected to a 6.0 Ω resistor and a 4.0 Ω resistor in parallel. Calculate the current in each branch and the total current from the supply. (1) Each branch has the full 12 V across it. (2) 6.0 Ω branch: I = V ÷ R = 12 ÷ 6.0 = 2.0 A. (3) 4.0 Ω branch: I = V ÷ R = 12 ÷ 4.0 = 3.0 A. (4) Total current: 2.0 + 3.0 = 5.0 A. Answer: 5.0 A in total (2.0 A and 3.0 A in the branches). Tip: The branch currents add up to the current from the supply.

## Slide 8
Worked example: Current splits and rejoins
Teach
A 12 V supply is connected to a 6.0 Ω resistor and a 4.0 Ω resistor in parallel. Calculate the current in each branch and the total current from the supply.
1
Each branch has the full 12 V across it.
2
6.0 Ω branch: I = V ÷ R = 12 ÷ 6.0 = 2.0 A.
3
4.0 Ω branch: I = V ÷ R = 12 ÷ 4.0 = 3.0 A.
4
Total current: 2.0 + 3.0 = 5.0 A.
Answer 5.0 A in total (2.0 A and 3.0 A in the branches)
Notes: Teach — Current splits and rejoins. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. Think of a river flowing round an island. The water splits between the two channels and joins up again downstream: the water in the two channels adds up to the water in the river. Current behaves the same way at a junction. The total current from the supply is the sum of the currents in the separate branches: I(total) = I₁ + I₂ + …. A branch with a lower resistance takes a bigger share of the current. Worked example — model it step by step, thinking aloud: A 12 V supply is connected to a 6.0 Ω resistor and a 4.0 Ω resistor in parallel. Calculate the current in each branch and the total current from the supply. (1) Each branch has the full 12 V across it. (2) 6.0 Ω branch: I = V ÷ R = 12 ÷ 6.0 = 2.0 A. (3) 4.0 Ω branch: I = V ÷ R = 12 ÷ 4.0 = 3.0 A. (4) Total current: 2.0 + 3.0 = 5.0 A. Answer: 5.0 A in total (2.0 A and 3.0 A in the branches). Tip: The branch currents add up to the current from the supply.

## Slide 9
Resistance in parallel, and why homes use it
Teach
!
Tip Parallel total resistance is always less than the smallest branch resistance.
1
Adding a resistor in parallel gives the charge another path, so the total current from the supply increases.
2
Adding another lamp in parallel does not make the other lamps dimmer or brighter: each still has the full supply p.d. across it, so each keeps the same current.
3
Homes are wired in parallel for these reasons. Every appliance gets the full mains p.d., each one can be switched on and off on its own, and if one breaks the others keep working.
Notes: Teach — Resistance in parallel, and why homes use it. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. Adding a resistor in parallel gives the charge another path, so the total current from the supply increases. More current for the same p.d. means the total resistance of the circuit has gone down. The total resistance of resistors in parallel is always less than the smallest single resistance. You can find it from the supply: R(total) = V ÷ I(total). Adding another lamp in parallel does not make the other lamps dimmer or brighter: each still has the full supply p.d. across it, so each keeps the same current. What does change is the total current drawn from the supply, which goes up. Homes are wired in parallel for these reasons. Every appliance gets the full mains p.d., each one can be switched on and off on its own, and if one breaks the others keep working. Worked example — model it step by step, thinking aloud: In the 12 V circuit above, the total current is 5.0 A. Calculate the total resistance of the two resistors, and compare it with 4.0 Ω. (1) Use R = V ÷ I with the supply p.d. and the total current. (2) R(total) = 12 ÷ 5.0 = 2.4 Ω. (3) 2.4 Ω is less than 4.0 Ω, the smallest resistor, as expected for parallel. Answer: 2.4 Ω, which is less than the smallest resistor (4.0 Ω). Tip: Parallel total resistance is always less than the smallest branch resistance.

## Slide 10
Worked example: Resistance in parallel, and why homes use it
Teach
In the 12 V circuit above, the total current is 5.0 A. Calculate the total resistance of the two resistors, and compare it with 4.0 Ω.
1
Use R = V ÷ I with the supply p.d. and the total current.
2
R(total) = 12 ÷ 5.0 = 2.4 Ω.
3
2.4 Ω is less than 4.0 Ω, the smallest resistor, as expected for parallel.
Answer 2.4 Ω, which is less than the smallest resistor (4.0 Ω)
Notes: Teach — Resistance in parallel, and why homes use it. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. Adding a resistor in parallel gives the charge another path, so the total current from the supply increases. More current for the same p.d. means the total resistance of the circuit has gone down. The total resistance of resistors in parallel is always less than the smallest single resistance. You can find it from the supply: R(total) = V ÷ I(total). Adding another lamp in parallel does not make the other lamps dimmer or brighter: each still has the full supply p.d. across it, so each keeps the same current. What does change is the total current drawn from the supply, which goes up. Homes are wired in parallel for these reasons. Every appliance gets the full mains p.d., each one can be switched on and off on its own, and if one breaks the others keep working. Worked example — model it step by step, thinking aloud: In the 12 V circuit above, the total current is 5.0 A. Calculate the total resistance of the two resistors, and compare it with 4.0 Ω. (1) Use R = V ÷ I with the supply p.d. and the total current. (2) R(total) = 12 ÷ 5.0 = 2.4 Ω. (3) 2.4 Ω is less than 4.0 Ω, the smallest resistor, as expected for parallel. Answer: 2.4 Ω, which is less than the smallest resistor (4.0 Ω). Tip: Parallel total resistance is always less than the smallest branch resistance.

## Slide 11
Same task, three ways in: Branch currents and total current
3
Routes
1
Everyone
A 9.0 V battery is connected to a 3.0 Ω resistor and a 9.0 Ω resistor in parallel. Calculate the total current from the battery, in amps.
Answer: __________ A
1
Support
1 Each branch has the full battery p.d.
2 Find each branch current with I = V ÷ R.
3 Add the branch currents to get the total.
2
Core
Hint: Work out each branch on its own first, then add.
3
Stretch
Then: Explain why the 3.0 Ω branch takes three times the current of the 9.0 Ω branch.
Notes: Task 1: Branch currents and total current. Same task, three ways in: one destination for everyone; only the scaffold changes. Pupils take the lane their do-now score pointed to (3/3 Stretch, 2/3 Core, 0–1 Support) and may move up at any time. Start the pre-teach group first: they know the words and the passage, so set them going on the task before you turn to the rest. Recall before help: every pupil tries from memory before opening a lane. The task: A 9.0 V battery is connected to a 3.0 Ω resistor and a 9.0 Ω resistor in parallel. Calculate the total current from the battery, in amps. Support — work through the steps with the group: (1) Each branch has the full battery p.d. (2) Find each branch current with I = V ÷ R. (3) Add the branch currents to get the total. Parallel worked example for Support (model it, do not give the task answer): A 6.0 V battery is connected to a 2.0 Ω and a 3.0 Ω resistor in parallel. Calculate the total current. 2.0 Ω branch: I = 6.0 ÷ 2.0 = 3.0 A.; 3.0 Ω branch: I = 6.0 ÷ 3.0 = 2.0 A.; Total = 3.0 + 2.0 = 5.0 A.. Answer: 5.0 A. Core — reveal the hint only on request: Work out each branch on its own first, then add. Stretch — no help; when finished: Explain why the 3.0 Ω branch takes three times the current of the 9.0 Ω branch.

## Slide 12
The task: Adding a lamp in parallel
4
Same task
2
Two identical lamps are in parallel with a battery. A third identical lamp is added on a new branch. What happens?
A The current from the battery increases, and the first two lamps stay the same brightness.
B The current from the battery stays the same, and it is shared between three lamps.
C The current from the battery increases, and the first two lamps get brighter.
D The current from the battery decreases, and all the lamps get dimmer.
Notes: Task 2: Adding a lamp in parallel. Same task, three ways in: one destination for everyone; only the scaffold changes. Pupils take the lane their do-now score pointed to (3/3 Stretch, 2/3 Core, 0–1 Support) and may move up at any time. Start the pre-teach group first: they know the words and the passage, so set them going on the task before you turn to the rest. Recall before help: every pupil tries from memory before opening a lane. The task: Two identical lamps are in parallel with a battery. A third identical lamp is added on a new branch. What happens? Support — work through the steps with the group: (1) What p.d. does each branch get? (The full supply.) (2) If a lamp's p.d. does not change, its current and brightness do not change. (3) The new branch adds its own current to the total. Parallel worked example for Support (model it, do not give the task answer): Two lamps are in series with a battery. A third identical lamp is added in series. What happens? The total resistance increases.; So the current in the loop decreases.; The p.d. is shared three ways, so every lamp gets dimmer.. Answer: The current decreases and all the lamps get dimmer.. Core — reveal the hint only on request: In parallel, each branch gets the full supply p.d., whatever the other branches do. Stretch — no help; when finished: Explain why the total resistance of the circuit falls when the third lamp is added, even though you have added another component.

## Slide 13
Same task, three ways in: Adding a lamp in parallel
3
Routes
2
Everyone
Two identical lamps are in parallel with a battery. A third identical lamp is added on a new branch. What happens?
1
Support
1 What p.d. does each branch get? (The full supply.)
2 If a lamp's p.d. does not change, its current and brightness do not change.
3 The new branch adds its own current to the total.
2
Core
Hint: In parallel, each branch gets the full supply p.d., whatever the other branches do.
3
Stretch
Then: Explain why the total resistance of the circuit falls when the third lamp is added, even though you have added another component.
Notes: Task 2: Adding a lamp in parallel. Same task, three ways in: one destination for everyone; only the scaffold changes. Pupils take the lane their do-now score pointed to (3/3 Stretch, 2/3 Core, 0–1 Support) and may move up at any time. Start the pre-teach group first: they know the words and the passage, so set them going on the task before you turn to the rest. Recall before help: every pupil tries from memory before opening a lane. The task: Two identical lamps are in parallel with a battery. A third identical lamp is added on a new branch. What happens? Support — work through the steps with the group: (1) What p.d. does each branch get? (The full supply.) (2) If a lamp's p.d. does not change, its current and brightness do not change. (3) The new branch adds its own current to the total. Parallel worked example for Support (model it, do not give the task answer): Two lamps are in series with a battery. A third identical lamp is added in series. What happens? The total resistance increases.; So the current in the loop decreases.; The p.d. is shared three ways, so every lamp gets dimmer.. Answer: The current decreases and all the lamps get dimmer.. Core — reveal the hint only on request: In parallel, each branch gets the full supply p.d., whatever the other branches do. Stretch — no help; when finished: Explain why the total resistance of the circuit falls when the third lamp is added, even though you have added another component.

## Slide 14
Exit ticket
Exit
Exit
A 12 V supply is connected to a 4.0 Ω resistor and a 12 Ω resistor in parallel. Calculate the total resistance of the circuit, in ohms.
My answer (Ω):
Notes: Exit ticket — individual, silent, on a slip or mini-whiteboard. Recall before help: no notes, no lanes, no hints. Collect before pupils leave. Question: A 12 V supply is connected to a 4.0 Ω resistor and a 12 Ω resistor in parallel. Calculate the total resistance of the circuit, in ohms. Answer: 3 Ω. Total current 4.0 A from 12 V gives R(total) = 3.0 Ω, which is less than the smallest resistor, as it must be in parallel. Source of this question: module 3 task ("Total resistance in parallel") from the manifest. Sort the slips: correct → ready to move on; incorrect → start next lesson in the pre-teach group, with the read-along and the Support lane. Same destination next time.

## Slide 15
Answers: Branch currents and total current
4
Check
Answer
A 9.0 V battery is connected to a 3.0 Ω resistor and a 9.0 Ω resistor in parallel. Calculate the total current from the battery, in amps.
4 A
Why
Branch currents 3.0 A and 1.0 A add up to 4.0 A from the battery.
Notes: Answers — task 1: Branch currents and total current. Reveal the answer; pupils mark their own work in a different colour, then read the "why" together. Same destination for every lane, so one answer serves the whole class. Answer: 4 A Why: Branch currents 3.0 A and 1.0 A add up to 4.0 A from the battery. Ask a Support pupil to explain one step, and a Stretch pupil to share their extension.

## Slide 16
Answers: Adding a lamp in parallel
4
Check
Answer
Two identical lamps are in parallel with a battery. A third identical lamp is added on a new branch. What happens?
A The current from the battery increases, and the first two lamps stay the same brightness.
Why
Parallel branches are independent: the old lamps keep their p.d., current and brightness; the battery supplies more current in total.
Notes: Answers — task 2: Adding a lamp in parallel. Reveal the answer; pupils mark their own work in a different colour, then read the "why" together. Same destination for every lane, so one answer serves the whole class. Answer: A The current from the battery increases, and the first two lamps stay the same brightness. Why: Parallel branches are independent: the old lamps keep their p.d., current and brightness; the battery supplies more current in total. Ask a Support pupil to explain one step, and a Stretch pupil to share their extension.

## Slide 17
Answers: Exit ticket
4
Check
Answer
A 12 V supply is connected to a 4.0 Ω resistor and a 12 Ω resistor in parallel. Calculate the total resistance of the circuit, in ohms.
3 Ω
Why
Total current 4.0 A from 12 V gives R(total) = 3.0 Ω, which is less than the smallest resistor, as it must be in parallel.
Notes: Answers — exit ticket: Exit ticket. Reveal the answer; pupils mark their own work in a different colour, then read the "why" together. Same destination for every lane, so one answer serves the whole class. Answer: 3 Ω Why: Total current 4.0 A from 12 V gives R(total) = 3.0 Ω, which is less than the smallest resistor, as it must be in parallel. Ask a Support pupil to explain one step, and a Stretch pupil to share their extension.