## Slide 1
6
Geography · Year 10
Chapter 6/6
Physical Landscapes in the UK: Rivers and Coasts · AQA 8035
Flooding, hydrographs and managing the river
Lessons covered
17 River flooding and hydrographs
18 Factors increasing flood risk and hydrographs
19 Flood management strategies
20 Case study of flood management at Banbury
?
Big question
How do waves and rivers shape the UK's coasts and valleys, and how should we manage the risks they bring?
Notes: Chapter 6 of 6: Flooding, hydrographs and managing the river. Why rivers flood, how a hydrograph shows a river's response to a storm, which drainage basins flood fastest, and the hard and soft ways of managing floods, with Banbury as your case study. This deck covers the department's lessons: 17 (River flooding and hydrographs: What causes a river to flood, and how does a hydrograph show a river's response to rainfall?); 18 (Factors increasing flood risk and hydrographs: Which physical and human factors increase flood risk, and what makes a hydrograph flashy or gentle?); 19 (Flood management strategies: What hard and soft engineering strategies are used to manage river floods, and what are their costs and benefits?); 20 (Case study of flood management at Banbury: Where is Banbury, what has been done to reduce its flood risk, and what are the social, economic and environmental issues?). Read the big question aloud: "How do waves and rivers shape the UK's coasts and valleys, and how should we manage the risks they bring?" We come back to it at the exit ticket. Before this lesson the pre-teach group has heard the read-along and met the key words; today they lead the reading. Lesson shape: do now (recall before any help), key words, read-along, teach, then the same task three ways in (Support, Core, Stretch), exit ticket, answers. Every pupil works towards the same destination.

## Slide 2
Do now: three from memory
2
Gate
1
Work it out
On a hydrograph, peak rainfall was at 06:00 and peak discharge was at 15:00. What was the lag time, in hours?
Answer: ________ hours
2
Choose one
Which of these is a human cause of flooding?
A Relief of the drainage basin
B Precipitation
C Rock type
D Urbanisation
3
Fill the gap
A flashy hydrograph has a ___ lag time and a high peak discharge.
Word bank: short · long · zero
Notes: Do now — retrieval. Silent, no notes, no help: recall comes before any support. Give about four minutes. 1. On a hydrograph, peak rainfall was at 06:00 and peak discharge was at 15:00. What was the lag time, in hours? → 9 hours 2. Which of these is a human cause of flooding? → D Urbanisation 3. A flashy hydrograph has a ___ lag time and a high peak discharge. → short Circulate: who gets 3/3 (Stretch route), 2/3 (Core), 0–1 (Support)? Use this to route pupils later in the lesson.

## Slide 3
Answers
2
Gate
1
Answer
9 hours
On a hydrograph, peak rainfall was at 06:00 and peak discharge was at 15:00. What was the lag time, in hours?
Lag time is the time between peak rainfall and peak discharge: 15:00 − 06:00 = 9 hours.
2
Answer
D Urbanisation
Which of these is a human cause of flooding?
Urbanisation is people covering the land in impermeable surfaces and drains, so rain reaches the river fast. The other three are physical.
3
Answer
short
A flashy hydrograph has a ___ lag time and a high peak discharge.
Flashy means the river responds quickly: the peak discharge comes soon after the peak rainfall.
Notes: Answers — pupils mark their own in a different colour, then hands up for 3/3, 2/3, 1/3. 1. 9 hours. Lag time is the time between peak rainfall and peak discharge: 15:00 − 06:00 = 9 hours. 2. D Urbanisation. Urbanisation is people covering the land in impermeable surfaces and drains, so rain reaches the river fast. The other three are physical. 3. short. Flashy means the river responds quickly: the peak discharge comes soon after the peak rainfall. Say the route each score points to: 3/3 Stretch, 2/3 Core, 0–1 Support. Pupils may choose to move up.

## Slide 4
Key words (1 of 2)
1
Pre-teach
1
discharge
the amount of water passing a point on a river each second
After the storm the river's discharge doubled.
2
hydrograph
a graph showing how a river's discharge changes after rain
The hydrograph showed a sharp peak six hours after the storm.
3
lag time
the time between the heaviest rain and the highest discharge
A short lag time means the river rises quickly.
Notes: Key words. Ask the pre-teach group first: they met these words before the lesson, so they give the meaning before anyone else. For each word: say it, pupils repeat it, read the meaning, then read the example sentence together. • discharge: the amount of water passing a point on a river each second. Example: "After the storm the river's discharge doubled." • hydrograph: a graph showing how a river's discharge changes after rain. Example: "The hydrograph showed a sharp peak six hours after the storm." • lag time: the time between the heaviest rain and the highest discharge. Example: "A short lag time means the river rises quickly." Recall before help: cover the meanings and ask pupils to define one word from memory before moving on.

## Slide 5
Key words (2 of 2)
1
Pre-teach
4
peak discharge
the highest discharge the river reaches after rain
Peak discharge was far above the level of the banks.
5
floodplain zoning
deciding what may be built on land that could flood
Floodplain zoning keeps houses away from the riverside.
6
afforestation
planting trees
Afforestation in the upper basin slows water reaching the river.
Notes: Key words. Ask the pre-teach group first: they met these words before the lesson, so they give the meaning before anyone else. For each word: say it, pupils repeat it, read the meaning, then read the example sentence together. • peak discharge: the highest discharge the river reaches after rain. Example: "Peak discharge was far above the level of the banks." • floodplain zoning: deciding what may be built on land that could flood. Example: "Floodplain zoning keeps houses away from the riverside." • afforestation: planting trees. Example: "Afforestation in the upper basin slows water reaching the river." Recall before help: cover the meanings and ask pupils to define one word from memory before moving on.

## Slide 6
Read-along (1 of 2)
1
Pre-teach
Read
Read together;
pupils who were pre-taught lead
1 A river floods when more water enters it than its channel can hold.
2 Heavy rain, steep slopes and impermeable rock all make floods more likely.
3 Melting ice and snow can add to the water too.
4 People make floods worse by building towns and cutting down trees.
5 Hard surfaces and drains send rain into the river quickly.
6 A hydrograph is a graph showing how a river responds to a storm.
Notes: Read together; pupils who were pre-taught lead. The pre-teach group heard this passage (with highlighted audio in the ebook) before the lesson, so invite them to read each sentence aloud first; everyone else follows with a finger, then echo-reads it. Key words are in bold: pause on each and ask for its meaning. Sentences 1–6 of 12: 1. A river floods when more water enters it than its channel can hold. 2. Heavy rain, steep slopes and impermeable rock all make floods more likely. 3. Melting ice and snow can add to the water too. 4. People make floods worse by building towns and cutting down trees. 5. Hard surfaces and drains send rain into the river quickly. 6. A hydrograph is a graph showing how a river responds to a storm. In the ebook the audio highlights each sentence as it is read.

## Slide 7
Read-along (2 of 2)
1
Pre-teach
Read
Read together;
pupils who were pre-taught lead
7 Discharge is the amount of water passing a point, measured in cumecs.
8 Lag time is the gap between the heaviest rain and the highest discharge.
9 A flashy hydrograph has a short lag time and a high peak.
10 Floods can be managed with hard engineering, such as dams and embankments.
11 Soft engineering includes planting trees and flood warnings.
12 Banbury is your case study of flood management in the UK.
Notes: Read together; pupils who were pre-taught lead. The pre-teach group heard this passage (with highlighted audio in the ebook) before the lesson, so invite them to read each sentence aloud first; everyone else follows with a finger, then echo-reads it. Key words are in bold: pause on each and ask for its meaning. Sentences 7–12 of 12: 7. Discharge is the amount of water passing a point, measured in cumecs. 8. Lag time is the gap between the heaviest rain and the highest discharge. 9. A flashy hydrograph has a short lag time and a high peak. 10. Floods can be managed with hard engineering, such as dams and embankments. 11. Soft engineering includes planting trees and flood warnings. 12. Banbury is your case study of flood management in the UK. In the ebook the audio highlights each sentence as it is read.

## Slide 8
Why rivers flood
Teach
!
Tip Sort first, explain second. Say whether a factor is physical or human, then say how it gets water into the river faster.
1
A river floods when its discharge is greater than its channel can hold, so water overflows the banks onto the floodplain.
2
Other causes are human. Urbanisation covers the land in impermeable concrete and tarmac, and drains and sewers carry rain straight to the river.
3
Flood risk is the combination of these factors. A steep, impermeable, deforested basin with a town in it floods quickly and badly after heavy rain.
Notes: Teach — Why rivers flood. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. A river floods when its discharge is greater than its channel can hold, so water overflows the banks onto the floodplain. Some of the causes are physical. Precipitation is the main one: heavy or prolonged rain, or a sudden thaw of snow and ice (an indirect cause, because the melt adds water that did not fall as rain that day). Geology matters: impermeable rock such as granite or clay does not let water soak in, so it runs straight off into the river. The relief of the drainage basin matters: on steep slopes water reaches the river quickly. A high drainage density, with many streams in the basin, delivers water to the main river faster. Other causes are human. Urbanisation covers the land in impermeable concrete and tarmac, and drains and sewers carry rain straight to the river. Deforestation removes trees that would intercept rain on their leaves and take up water through their roots, so more water reaches the river faster. Agriculture can leave soil bare or compacted, so rain runs off rather than soaking in. Your sorting task in class put precipitation, rock type, relief, drainage density and ice melt in the physical column, and urbanisation, deforestation and agriculture in the human column. Flood risk is the combination of these factors. A steep, impermeable, deforested basin with a town in it floods quickly and badly after heavy rain. A gentle, permeable, forested basin soaks the same rain up and releases it slowly. Tip: Sort first, explain second. Say whether a factor is physical or human, then say how it gets water into the river faster.

## Slide 9
Reading a hydrograph
Teach
!
Tip Read the two peaks, not the start of the rain. Lag time is peak to peak.
1
A hydrograph is a graph that shows how a river responds to a storm.
2
A flashy hydrograph has a short lag time and a high peak discharge: the river rises fast and high, so flooding is likely.
Notes: Teach — Reading a hydrograph. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. A hydrograph is a graph that shows how a river responds to a storm. Time runs along the bottom. Rainfall is shown as bars, and the river's discharge as a line. Discharge is the amount of water passing a given point on the river, measured in cubic metres per second, written cumecs. The line rises after the rain (the rising limb), reaches its peak discharge, the highest discharge after the rainfall, and then falls (the falling limb). Lag time is the difference in time between peak rainfall and peak discharge. A flashy hydrograph has a short lag time and a high peak discharge: the river rises fast and high, so flooding is likely. A gentle hydrograph has a longer lag time and a lower peak: the water arrives slowly and the river copes. Which one a basin produces depends on the same factors as flood risk. Basin A, with the flashy hydrograph, has steep slopes, impermeable rock, very thin soil, thin grass and moorland, urban land use, limited use of the river and a high drainage density. Basin B, with the gentle hydrograph, has gentle slopes, permeable rock, deep soil, forest, rural land use, a river used for industry with a dam built on it, and a low drainage density. Worked example — model it step by step, thinking aloud: On a hydrograph, peak rainfall was at 03:00 and peak discharge was at 11:00. What was the lag time? (1) Lag time is the time from peak rainfall to peak discharge, not from the start of the rain. (2) Peak rainfall 03:00; peak discharge 11:00. (3) 11 − 3 = 8. (4) Lag time = 8 hours. A lag time this short, on a big storm, suggests a fairly flashy basin. Answer: 8 hours. Tip: Read the two peaks, not the start of the rain. Lag time is peak to peak.

## Slide 10
Worked example: Reading a hydrograph
Teach
On a hydrograph, peak rainfall was at 03:00 and peak discharge was at 11:00. What was the lag time?
1
Lag time is the time from peak rainfall to peak discharge, not from the start of the rain.
2
Peak rainfall 03:00; peak discharge 11:00.
3
11 − 3 = 8.
4
Lag time = 8 hours. A lag time this short, on a big storm, suggests a fairly flashy basin.
Answer 8 hours
Notes: Teach — Reading a hydrograph. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. A hydrograph is a graph that shows how a river responds to a storm. Time runs along the bottom. Rainfall is shown as bars, and the river's discharge as a line. Discharge is the amount of water passing a given point on the river, measured in cubic metres per second, written cumecs. The line rises after the rain (the rising limb), reaches its peak discharge, the highest discharge after the rainfall, and then falls (the falling limb). Lag time is the difference in time between peak rainfall and peak discharge. A flashy hydrograph has a short lag time and a high peak discharge: the river rises fast and high, so flooding is likely. A gentle hydrograph has a longer lag time and a lower peak: the water arrives slowly and the river copes. Which one a basin produces depends on the same factors as flood risk. Basin A, with the flashy hydrograph, has steep slopes, impermeable rock, very thin soil, thin grass and moorland, urban land use, limited use of the river and a high drainage density. Basin B, with the gentle hydrograph, has gentle slopes, permeable rock, deep soil, forest, rural land use, a river used for industry with a dam built on it, and a low drainage density. Worked example — model it step by step, thinking aloud: On a hydrograph, peak rainfall was at 03:00 and peak discharge was at 11:00. What was the lag time? (1) Lag time is the time from peak rainfall to peak discharge, not from the start of the rain. (2) Peak rainfall 03:00; peak discharge 11:00. (3) 11 − 3 = 8. (4) Lag time = 8 hours. A lag time this short, on a big storm, suggests a fairly flashy basin. Answer: 8 hours. Tip: Read the two peaks, not the start of the rain. Lag time is peak to peak.

## Slide 11
Managing floods: hard and soft engineering
Teach
!
Tip Four hard, four soft: dams, straightening, embankments, relief channels; zoning, afforestation, warnings, restoration. Learn one cost and one benefit for each.
As at the coast, flood management divides into hard and soft engineering.
The soft strategies are floodplain zoning, which restricts building on land likely to flood so that only low-value uses such as playing fields sit beside the river; afforestation, planting trees to intercept rain and slow its journey to the river; flood warnings, which give people time to move belongings and themselves; and river restoration, which returns a straightened river to a natural meandering course so its floodplain can store water.
In your lesson you rated each strategy on a thermometer for its costs and benefits and added case studies where you could.
Notes: Teach — Managing floods: hard and soft engineering. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. As at the coast, flood management divides into hard and soft engineering. The hard strategies are dams and reservoirs, which hold water back in the upper course and release it slowly; channel straightening, which cuts off meanders so water leaves the area faster; embankments, which raise the banks so the channel holds more water; and flood relief channels, which carry excess water around a town. Hard engineering is expensive, can look unnatural and can simply move the flood problem downstream, but it protects valuable property reliably. The soft strategies are floodplain zoning, which restricts building on land likely to flood so that only low-value uses such as playing fields sit beside the river; afforestation, planting trees to intercept rain and slow its journey to the river; flood warnings, which give people time to move belongings and themselves; and river restoration, which returns a straightened river to a natural meandering course so its floodplain can store water. Soft strategies are cheaper and more sustainable, but they do not stop a flood on their own, and zoning cannot help a town that is already built. In your lesson you rated each strategy on a thermometer for its costs and benefits and added case studies where you could. The best schemes, like the one at Banbury, combine hard and soft methods. Tip: Four hard, four soft: dams, straightening, embankments, relief channels; zoning, afforestation, warnings, restoration. Learn one cost and one benefit for each.

## Slide 12
Case study: flood management at Banbury
Teach
!
Tip Where, why, what, and the social, economic and environmental issues: four headings for every management case study in this unit.
1
Banbury is your named example of a UK flood management scheme.
2
Use your notes to build a one-page summary with those four headings.
3
A case-study answer scores when it is specific. Name the town, name a measure, give a number or a place, and then make the geographical point.
Notes: Teach — Case study: flood management at Banbury. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. Banbury is your named example of a UK flood management scheme. In class you used pages 130 and 131 of the textbook to answer four questions, and those four questions are exactly what the exam can ask: where is Banbury; why did it need protecting from floods; what has been done to reduce the flood risk; and what are the social, economic and environmental issues of the scheme. Use your notes to build a one-page summary with those four headings. Under what has been done, sort the measures into hard and soft engineering. Under the issues, give one social (people and homes), one economic (money and jobs) and one environmental (wildlife and landscape) point, and say whether each is a cost or a benefit of the scheme. A case-study answer scores when it is specific. Name the town, name a measure, give a number or a place, and then make the geographical point. A general answer about flood management with Banbury written at the top will not reach the top level. Tip: Where, why, what, and the social, economic and environmental issues: four headings for every management case study in this unit.

## Slide 13
The task: Hydrograph words
4
Same task
1
Match each hydrograph term to its meaning.
1
Hydrograph
A
The highest discharge the river reaches after the rainfall
2
Discharge
B
The amount of water passing a point on the river, in cumecs
3
Peak discharge
C
The time between peak rainfall and peak discharge
4
Lag time
D
A graph showing how a river responds to a storm
Notes: Task 1: Hydrograph words. Same task, three ways in: one destination for everyone; only the scaffold changes. Pupils take the lane their do-now score pointed to (3/3 Stretch, 2/3 Core, 0–1 Support) and may move up at any time. Start the pre-teach group first: they know the words and the passage, so set them going on the task before you turn to the rest. Recall before help: every pupil tries from memory before opening a lane. The task: Match each hydrograph term to its meaning. Support — work through the steps with the group: (1) One term is the whole graph. (2) One term is a time, so its meaning must mention time. (3) Two terms contain the word discharge: one is the amount in general, one is the highest point. (4) The unit cumecs goes with the general measurement. Parallel worked example for Support (model it, do not give the task answer): Match: rising limb, falling limb. Choices: the part of the line where discharge is going down after the peak; the part of the line where discharge is going up towards the peak. Rising goes up, before the peak.; Falling goes down, after the peak.. Answer: Rising limb: discharge going up towards the peak. Falling limb: discharge going down after the peak.. Core — reveal the hint only on request: One is the graph, one is a time, and two are amounts of water (one of them the biggest). Stretch — no help; when finished: Explain what a short lag time tells you about the drainage basin, giving two possible reasons.

## Slide 14
Same task, three ways in: Hydrograph words
3
Routes
1
Everyone
Match each hydrograph term to its meaning.
1
Support
1 One term is the whole graph.
2 One term is a time, so its meaning must mention time.
3 Two terms contain the word discharge: one is the amount in general, one is the highest point.
4 The unit cumecs goes with the general measurement.
2
Core
Hint: One is the graph, one is a time, and two are amounts of water (one of them the biggest).
3
Stretch
Then: Explain what a short lag time tells you about the drainage basin, giving two possible reasons.
Notes: Task 1: Hydrograph words. Same task, three ways in: one destination for everyone; only the scaffold changes. Pupils take the lane their do-now score pointed to (3/3 Stretch, 2/3 Core, 0–1 Support) and may move up at any time. Start the pre-teach group first: they know the words and the passage, so set them going on the task before you turn to the rest. Recall before help: every pupil tries from memory before opening a lane. The task: Match each hydrograph term to its meaning. Support — work through the steps with the group: (1) One term is the whole graph. (2) One term is a time, so its meaning must mention time. (3) Two terms contain the word discharge: one is the amount in general, one is the highest point. (4) The unit cumecs goes with the general measurement. Parallel worked example for Support (model it, do not give the task answer): Match: rising limb, falling limb. Choices: the part of the line where discharge is going down after the peak; the part of the line where discharge is going up towards the peak. Rising goes up, before the peak.; Falling goes down, after the peak.. Answer: Rising limb: discharge going up towards the peak. Falling limb: discharge going down after the peak.. Core — reveal the hint only on request: One is the graph, one is a time, and two are amounts of water (one of them the biggest). Stretch — no help; when finished: Explain what a short lag time tells you about the drainage basin, giving two possible reasons.

## Slide 15
Same task, three ways in: How much water is that?
3
Routes
2
Everyone
A river's discharge is 240 cumecs (cubic metres per second). How many cubic metres of water pass the gauging station in one minute?
Answer: __________ m³
1
Support
1 Cumecs means cubic metres per second: 240 cubic metres go past every second.
2 How many seconds are there in a minute? 60.
3 Multiply: 240 × 60.
4 240 × 6 = 1440, so 240 × 60 = 14 400.
2
Core
Hint: Per second to per minute: multiply by 60.
3
Stretch
Then: A swimming pool holds about 2 500 cubic metres. Estimate how long the river at 240 cumecs would take to fill it, and show your working.
Notes: Task 2: How much water is that?. Same task, three ways in: one destination for everyone; only the scaffold changes. Pupils take the lane their do-now score pointed to (3/3 Stretch, 2/3 Core, 0–1 Support) and may move up at any time. Start the pre-teach group first: they know the words and the passage, so set them going on the task before you turn to the rest. Recall before help: every pupil tries from memory before opening a lane. The task: A river's discharge is 240 cumecs (cubic metres per second). How many cubic metres of water pass the gauging station in one minute? Support — work through the steps with the group: (1) Cumecs means cubic metres per second: 240 cubic metres go past every second. (2) How many seconds are there in a minute? 60. (3) Multiply: 240 × 60. (4) 240 × 6 = 1440, so 240 × 60 = 14 400. Parallel worked example for Support (model it, do not give the task answer): A stream has a discharge of 15 cumecs. How many cubic metres pass in one minute? 15 cubic metres every second.; 60 seconds in a minute.; 15 × 60 = 900.. Answer: 900 cubic metres. Core — reveal the hint only on request: Per second to per minute: multiply by 60. Stretch — no help; when finished: A swimming pool holds about 2 500 cubic metres. Estimate how long the river at 240 cumecs would take to fill it, and show your working.

## Slide 16
Exit ticket
Exit
Exit
On a hydrograph, peak rainfall was at 06:00 and peak discharge was at 15:00. What was the lag time, in hours?
My answer (hours):
Notes: Exit ticket — individual, silent, on a slip or mini-whiteboard. Recall before help: no notes, no lanes, no hints. Collect before pupils leave. Question: On a hydrograph, peak rainfall was at 06:00 and peak discharge was at 15:00. What was the lag time, in hours? Answer: 9 hours. Lag time is the time between peak rainfall and peak discharge: 15:00 − 06:00 = 9 hours. Source of this question: gate item 1 re-asked (options rotated) — this chapter has no third quick-check module. The ebook also holds task 3, "People and floods", for homework or the next lesson's do now. Sort the slips: correct → ready to move on; incorrect → start next lesson in the pre-teach group, with the read-along and the Support lane. Same destination next time.

## Slide 17
Answers: Hydrograph words
4
Check
Answer
1 Hydrograph → D A graph showing how a river responds to a storm
2 Discharge → B The amount of water passing a point on the river, in cumecs
3 Peak discharge → A The highest discharge the river reaches after the rainfall
4 Lag time → C The time between peak rainfall and peak discharge
Why
The hydrograph is the graph; discharge is the amount of water per second (cumecs); peak discharge is its highest value; lag time is peak rainfall to peak discharge.
Notes: Answers — task 1: Hydrograph words. Reveal the answer; pupils mark their own work in a different colour, then read the "why" together. Same destination for every lane, so one answer serves the whole class. Answer: Hydrograph → D A graph showing how a river responds to a storm; Discharge → B The amount of water passing a point on the river, in cumecs; Peak discharge → A The highest discharge the river reaches after the rainfall; Lag time → C The time between peak rainfall and peak discharge Why: The hydrograph is the graph; discharge is the amount of water per second (cumecs); peak discharge is its highest value; lag time is peak rainfall to peak discharge. Ask a Support pupil to explain one step, and a Stretch pupil to share their extension.

## Slide 18
Answers: How much water is that?
4
Check
Answer
A river's discharge is 240 cumecs (cubic metres per second). How many cubic metres of water pass the gauging station in one minute?
14 400 m³
Why
240 cubic metres pass every second; 60 seconds make a minute; 240 × 60 = 14 400 cubic metres.
Notes: Answers — task 2: How much water is that?. Reveal the answer; pupils mark their own work in a different colour, then read the "why" together. Same destination for every lane, so one answer serves the whole class. Answer: 14 400 m³ Why: 240 cubic metres pass every second; 60 seconds make a minute; 240 × 60 = 14 400 cubic metres. Ask a Support pupil to explain one step, and a Stretch pupil to share their extension.

## Slide 19
Answers: Exit ticket
4
Check
Answer
On a hydrograph, peak rainfall was at 06:00 and peak discharge was at 15:00. What was the lag time, in hours?
9 hours
Why
Lag time is the time between peak rainfall and peak discharge: 15:00 − 06:00 = 9 hours.
Notes: Answers — exit ticket: Exit ticket. Reveal the answer; pupils mark their own work in a different colour, then read the "why" together. Same destination for every lane, so one answer serves the whole class. Answer: 9 hours Why: Lag time is the time between peak rainfall and peak discharge: 15:00 − 06:00 = 9 hours. Ask a Support pupil to explain one step, and a Stretch pupil to share their extension.