## Slide 1
6
Geography · Year 7
Chapter 6/6
Water on Land: Rivers · AQA KS3 → 8035
Managing floods: protecting people and places
Lessons covered
12 Flood defence systems
13 Revision, end-of-unit test and feedback
?
Big question
How does water shape the land, why do rivers flood, and what can people do to reduce the risk and the damage?
Notes: Chapter 6 of 6: Managing floods: protecting people and places. Short-term and long-term ways of coping with floods, how the Thames Barrier protects London, how to choose a defence, and how to show what you know in the test. This deck covers the department's lessons: 12 (Flood defence systems: How can people cope with floods in the short term and the long term?); 13 (Revision, end-of-unit test and feedback: Can you describe and explain what you have learned about rivers and flooding?). Read the big question aloud: "How does water shape the land, why do rivers flood, and what can people do to reduce the risk and the damage?" We come back to it at the exit ticket. Before this lesson the pre-teach group has heard the read-along and met the key words; today they lead the reading. Lesson shape: do now (recall before any help), key words, read-along, teach, then the same task three ways in (Support, Core, Stretch), exit ticket, answers. Every pupil works towards the same destination.

## Slide 2
Do now: three from memory
2
Gate
1
Choose one
Which of these is a SHORT-term way of coping with a flood?
A Building a flood wall along the river
B Putting sandbags across doorways
C Planting trees in the drainage basin
D Building the Thames Barrier
2
Work it out
The Thames Barrier's gates can take between 15 and 90 minutes to close. What is the difference, in minutes, between the slowest and the quickest closing time?
Answer: ________ minutes
3
Fill the gap
The Thames Barrier has ___ gates.
Word bank: ten · five · twenty
Notes: Do now — retrieval. Silent, no notes, no help: recall comes before any support. Give about four minutes. 1. Which of these is a SHORT-term way of coping with a flood? → B Putting sandbags across doorways 2. The Thames Barrier's gates can take between 15 and 90 minutes to close. What is the difference, in minutes, between the slowest and the quickest closing time? → 75 minutes 3. The Thames Barrier has ___ gates. → ten Circulate: who gets 3/3 (Stretch route), 2/3 (Core), 0–1 (Support)? Use this to route pupils later in the lesson.

## Slide 3
Answers
2
Gate
1
Answer
B Putting sandbags across doorways
Which of these is a SHORT-term way of coping with a flood?
Sandbags are put down just before or during a flood; the others take years to build or grow.
2
Answer
75 minutes
The Thames Barrier's gates can take between 15 and 90 minutes to close. What is the difference, in minutes, between the slowest and the quickest closing time?
90 − 15 = 75 minutes.
3
Answer
ten
The Thames Barrier has ___ gates.
The barrier has ten steel gates stretching about 500 m across the river.
Notes: Answers — pupils mark their own in a different colour, then hands up for 3/3, 2/3, 1/3. 1. B Putting sandbags across doorways. Sandbags are put down just before or during a flood; the others take years to build or grow. 2. 75 minutes. 90 − 15 = 75 minutes. 3. ten. The barrier has ten steel gates stretching about 500 m across the river. Say the route each score points to: 3/3 Stretch, 2/3 Core, 0–1 Support. Pupils may choose to move up.

## Slide 4
Key words
1
Pre-teach
Word
What it means
In a sentence
short-term
done just before or during a flood to cope with it
Sandbags are a short-term way to keep water out of a house.
long-term
built or planned to protect people for many years
A flood barrier is a long-term defence.
flood defence
anything built or done to stop flooding or reduce the damage
The town council paid for a new flood defence.
embankment
a raised bank built along a river so it can hold more water
The embankment kept the river off the road.
evaluate
to weigh up how good something is, using criteria
We had to evaluate three flood defences and choose the best.
Notes: Key words. Ask the pre-teach group first: they met these words before the lesson, so they give the meaning before anyone else. For each word: say it, pupils repeat it, read the meaning, then read the example sentence together. • short-term: done just before or during a flood to cope with it. Example: "Sandbags are a short-term way to keep water out of a house." • long-term: built or planned to protect people for many years. Example: "A flood barrier is a long-term defence." • flood defence: anything built or done to stop flooding or reduce the damage. Example: "The town council paid for a new flood defence." • embankment: a raised bank built along a river so it can hold more water. Example: "The embankment kept the river off the road." • evaluate: to weigh up how good something is, using criteria. Example: "We had to evaluate three flood defences and choose the best." Recall before help: cover the meanings and ask pupils to define one word from memory before moving on.

## Slide 5
Read-along (1 of 2)
1
Pre-teach
Read
Read together;
pupils who were pre-taught lead
1 People cannot stop the rain, but they can protect themselves from floods.
2 Short-term methods are used just before or during a flood.
3 Sandbags, flood warnings and moving people to safety are short-term.
4 Long-term methods take years to build but last for a long time.
5 Walls, embankments, dams, barriers and planting trees are long-term.
6 London is protected by the Thames Barrier.
Notes: Read together; pupils who were pre-taught lead. The pre-teach group heard this passage (with highlighted audio in the ebook) before the lesson, so invite them to read each sentence aloud first; everyone else follows with a finger, then echo-reads it. Key words are in bold: pause on each and ask for its meaning. Sentences 1–6 of 11: 1. People cannot stop the rain, but they can protect themselves from floods. 2. Short-term methods are used just before or during a flood. 3. Sandbags, flood warnings and moving people to safety are short-term. 4. Long-term methods take years to build but last for a long time. 5. Walls, embankments, dams, barriers and planting trees are long-term. 6. London is protected by the Thames Barrier. In the ebook the audio highlights each sentence as it is read.

## Slide 6
Read-along (2 of 2)
1
Pre-teach
Read
Read together;
pupils who were pre-taught lead
7 Its ten steel gates stretch about 500 m across the river.
8 It was first used in 1983.
9 When a high tide threatens London, the gates are raised.
10 Choosing a flood defence means weighing up cost, time and how well it works.
11 In your test, describe means say what, and explain means say why.
Notes: Read together; pupils who were pre-taught lead. The pre-teach group heard this passage (with highlighted audio in the ebook) before the lesson, so invite them to read each sentence aloud first; everyone else follows with a finger, then echo-reads it. Key words are in bold: pause on each and ask for its meaning. Sentences 7–11 of 11: 7. Its ten steel gates stretch about 500 m across the river. 8. It was first used in 1983. 9. When a high tide threatens London, the gates are raised. 10. Choosing a flood defence means weighing up cost, time and how well it works. 11. In your test, describe means say what, and explain means say why. In the ebook the audio highlights each sentence as it is read.

## Slide 7
Short-term and long-term ways of coping
Teach
!
Tip Short-term = during the emergency, cheap and quick. Long-term = built to last, expensive and slow. A good answer names one of each.
1
There are two kinds of flood protection. Short-term methods are used just before or during a flood to cope with it.
2
Long-term methods take years to plan and build, but protect people for a long time.
3
Notice the difference between reducing the risk of a flood happening (trees, dams, dredging) and reducing the damage when it does (warnings, sandbags, walls around homes).
Notes: Teach — Short-term and long-term ways of coping. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. There are two kinds of flood protection. Short-term methods are used just before or during a flood to cope with it. Flood warnings tell people a flood is coming. Sandbags across doorways keep water out of homes. People move valuables upstairs and, if needed, leave their homes for a safe place. Emergency services rescue people and bring food and clean water. Long-term methods take years to plan and build, but protect people for a long time. Embankments and flood walls raise the sides of the channel so it can hold more water. Dams hold water back upstream and let it out slowly. Barriers like the Thames Barrier close against high water. Dredging deepens the channel. Planting trees in the drainage basin increases infiltration and slows run-off. Planning rules can stop new homes being built on the floodplain. Notice the difference between reducing the risk of a flood happening (trees, dams, dredging) and reducing the damage when it does (warnings, sandbags, walls around homes). The best plans do both. Tip: Short-term = during the emergency, cheap and quick. Long-term = built to last, expensive and slow. A good answer names one of each.

## Slide 8
The Thames Barrier
Teach
1
London lies on the River Thames close to the sea, so a very high tide pushed up the river by a storm could flood the city.
2
The barrier has ten gates made of steel, stretching about 500 m across the river.
3
Engineers have thought about what could go wrong. If the computer that drives the barrier fails, the gates can be raised by hand with cranks.
Notes: Teach — The Thames Barrier. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. London lies on the River Thames close to the sea, so a very high tide pushed up the river by a storm could flood the city. The Thames Barrier was built to stop this. It was first used in 1983 and stands about 15 km downstream of the Houses of Parliament, at a spot chosen because the river banks are straight and the river bed is firm enough to build on. The barrier has ten gates made of steel, stretching about 500 m across the river. Normally the gates lie flat on the river bed so ships can pass. When a dangerous tide is forecast, they are rotated up to form a wall across the river. Closing can take between 15 and 90 minutes. The gates are hollow, and in an underspill position they can let a little water through, so that water does not pour over the top. Engineers have thought about what could go wrong. If the computer that drives the barrier fails, the gates can be raised by hand with cranks. An extra piston can lift each gate right out of the water so it can be checked for rust and damage. The barrier is a long-term defence: expensive to build, but protecting millions of people for decades. Worked example — model it step by step, thinking aloud: Explain how the Thames Barrier protects London from flooding. (4 marks) (1) Say what the danger is: a very high tide pushed up the river could flood London. (2) Describe the barrier: ten steel gates about 500 m across the river, normally flat on the bed. (3) Explain the action: when a high tide is forecast the gates are raised to make a wall, so the water cannot reach the city. (4) Add a detail that shows understanding: closing takes 15 to 90 minutes, and the gates can be cranked by hand if the computer fails. Answer: A storm tide coming up the Thames could flood London. The barrier's ten steel gates, about 500 m across, normally lie flat so ships can pass; when a high tide is forecast they are raised in 15 to 90 minutes to form a wall, so the water is held back. If the computer fails, the gates can be cranked by hand..

## Slide 9
Worked example: The Thames Barrier
Teach
Explain how the Thames Barrier protects London from flooding. (4 marks)
1
Say what the danger is: a very high tide pushed up the river could flood London.
2
Describe the barrier: ten steel gates about 500 m across the river, normally flat on the bed.
3
Explain the action: when a high tide is forecast the gates are raised to make a wall, so the water cannot reach the city.
4
Add a detail that shows understanding: closing takes 15 to 90 minutes, and the gates can be cranked by hand if the computer fails.
Answer A storm tide coming up the Thames could flood London. The barrier's ten steel gates, about 500 m across, normally lie flat so ships can pass; when a high tide is forecast they are raised in 15 to 90 minutes to form a wall, so the water is held back. If the computer fails, the gates can be cranked by hand.
Notes: Teach — The Thames Barrier. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. London lies on the River Thames close to the sea, so a very high tide pushed up the river by a storm could flood the city. The Thames Barrier was built to stop this. It was first used in 1983 and stands about 15 km downstream of the Houses of Parliament, at a spot chosen because the river banks are straight and the river bed is firm enough to build on. The barrier has ten gates made of steel, stretching about 500 m across the river. Normally the gates lie flat on the river bed so ships can pass. When a dangerous tide is forecast, they are rotated up to form a wall across the river. Closing can take between 15 and 90 minutes. The gates are hollow, and in an underspill position they can let a little water through, so that water does not pour over the top. Engineers have thought about what could go wrong. If the computer that drives the barrier fails, the gates can be raised by hand with cranks. An extra piston can lift each gate right out of the water so it can be checked for rust and damage. The barrier is a long-term defence: expensive to build, but protecting millions of people for decades. Worked example — model it step by step, thinking aloud: Explain how the Thames Barrier protects London from flooding. (4 marks) (1) Say what the danger is: a very high tide pushed up the river could flood London. (2) Describe the barrier: ten steel gates about 500 m across the river, normally flat on the bed. (3) Explain the action: when a high tide is forecast the gates are raised to make a wall, so the water cannot reach the city. (4) Add a detail that shows understanding: closing takes 15 to 90 minutes, and the gates can be cranked by hand if the computer fails. Answer: A storm tide coming up the Thames could flood London. The barrier's ten steel gates, about 500 m across, normally lie flat so ships can pass; when a high tide is forecast they are raised in 15 to 90 minutes to form a wall, so the water is held back. If the computer fails, the gates can be cranked by hand..

## Slide 10
You are in charge: choosing a flood defence
Teach
!
Tip Decision questions reward reasons, not choices. Every method you pick needs a because.
1
Imagine a new town is being planned near a river, and you have to protect it.
2
Two more criteria matter just as much. Sustainability: will it still work well in the future, as the climate changes and the town grows?
3
A strong decision names the methods chosen, gives a reason for each with because, and uses the words run-off, infiltration or overflow to explain how it works.
Notes: Teach — You are in charge: choosing a flood defence. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. Imagine a new town is being planned near a river, and you have to protect it. You cannot choose everything, because every defence has a cost. Geographers use criteria to decide. Cost: is it cheap or expensive to build and look after? Time: can it be done quickly, or will it take years? Effectiveness: does it reduce the risk of flooding, reduce the damage, or both? Two more criteria matter just as much. Sustainability: will it still work well in the future, as the climate changes and the town grows? Who benefits: homes, farms, transport, wildlife, or only some of these? An embankment may protect the town but push the flood water onto farms downstream. A strong decision names the methods chosen, gives a reason for each with because, and uses the words run-off, infiltration or overflow to explain how it works. For example: we chose to plant trees upstream because they increase infiltration, so less run-off reaches the river. Tip: Decision questions reward reasons, not choices. Every method you pick needs a because.

## Slide 11
Ready for the test
Teach
!
Tip Spell the key words correctly: precipitation, infiltration, saturated, hydraulic, meander, floodplain. SPaG marks count.
1
The end-of-unit test covers the whole unit: the water cycle and its key words, waterfalls and meanders, the physical and human causes of flooding, the effects of flooding in an LIC and an HIC, and the uses of rivers.
2
Two command words do most of the work. Describe means say what something is like or what happens, in order.
3
After the test you will get feedback. WWW means What Went Well, and EBI means Even Better If.
Notes: Teach — Ready for the test. Say it in your own words, then check understanding with a quick question: ask a pupil from the pre-teach group first, since they met these words and ideas before the lesson. Pupils try to recall before you re-explain. The end-of-unit test covers the whole unit: the water cycle and its key words, waterfalls and meanders, the physical and human causes of flooding, the effects of flooding in an LIC and an HIC, and the uses of rivers. It is marked out of 50, including spelling, punctuation and grammar, and lasts 60 minutes. Read the marks for each question and give that many points. Two command words do most of the work. Describe means say what something is like or what happens, in order. Explain means say why, using because. If a question says explain and you only describe, you lose most of the marks. For effects of a flood, sort your points into social, economic and environmental. After the test you will get feedback. WWW means What Went Well, and EBI means Even Better If. Use the model answers to correct your work in green pen, and write out any spelling you got wrong three times. That is how a mark becomes learning. Tip: Spell the key words correctly: precipitation, infiltration, saturated, hydraulic, meander, floodplain. SPaG marks count.

## Slide 12
The task: Built to last
4
Same task
1
A town beside a river wants protection that will last for many years. Which of these is a LONG-term flood defence?
A Sending out a flood warning
B Building an embankment along the river
C Moving furniture upstairs
D Putting sandbags in front of doors
Notes: Task 1: Built to last. Same task, three ways in: one destination for everyone; only the scaffold changes. Pupils take the lane their do-now score pointed to (3/3 Stretch, 2/3 Core, 0–1 Support) and may move up at any time. Start the pre-teach group first: they know the words and the passage, so set them going on the task before you turn to the rest. Recall before help: every pupil tries from memory before opening a lane. The task: A town beside a river wants protection that will last for many years. Which of these is a LONG-term flood defence? Support — work through the steps with the group: (1) Ask of each option: is it done in the hours before or during a flood, or built to stay for years? (2) Warnings, sandbags and moving things are all done as the flood arrives: short-term. (3) Something built along the river that stays there is long-term. (4) Pick the one that is built, not done. Parallel worked example for Support (model it, do not give the task answer): Which of these is a long-term flood defence: planting trees in the drainage basin, or rescuing people by boat? Rescuing people happens during the flood: short-term.; Trees take years to grow and then slow run-off for decades: long-term.. Answer: Planting trees in the drainage basin. Core — reveal the hint only on request: Long-term things are built or grown. Short-term things are done. Stretch — no help; when finished: Explain one disadvantage of an embankment for people living further downstream, and suggest a long-term method that avoids it.

## Slide 13
Same task, three ways in: Built to last
3
Routes
1
Everyone
Task 1 (on the last slide): Built to last
1
Support
1 Ask of each option: is it done in the hours before or during a flood, or built to stay for years?
2 Warnings, sandbags and moving things are all done as the flood arrives: short-term.
3 Something built along the river that stays there is long-term.
4 Pick the one that is built, not done.
2
Core
Hint: Long-term things are built or grown. Short-term things are done.
3
Stretch
Then: Explain one disadvantage of an embankment for people living further downstream, and suggest a long-term method that avoids it.
Notes: Task 1: Built to last. Same task, three ways in: one destination for everyone; only the scaffold changes. Pupils take the lane their do-now score pointed to (3/3 Stretch, 2/3 Core, 0–1 Support) and may move up at any time. Start the pre-teach group first: they know the words and the passage, so set them going on the task before you turn to the rest. Recall before help: every pupil tries from memory before opening a lane. The task: A town beside a river wants protection that will last for many years. Which of these is a LONG-term flood defence? Support — work through the steps with the group: (1) Ask of each option: is it done in the hours before or during a flood, or built to stay for years? (2) Warnings, sandbags and moving things are all done as the flood arrives: short-term. (3) Something built along the river that stays there is long-term. (4) Pick the one that is built, not done. Parallel worked example for Support (model it, do not give the task answer): Which of these is a long-term flood defence: planting trees in the drainage basin, or rescuing people by boat? Rescuing people happens during the flood: short-term.; Trees take years to grow and then slow run-off for decades: long-term.. Answer: Planting trees in the drainage basin. Core — reveal the hint only on request: Long-term things are built or grown. Short-term things are done. Stretch — no help; when finished: Explain one disadvantage of an embankment for people living further downstream, and suggest a long-term method that avoids it.

## Slide 14
The task: Years apart
4
Same task
2
The Thames Barrier was first used in 1983. The Somerset Levels flooded in 2014. How many years apart are these two dates?
Answer: __________ years
Notes: Task 2: Years apart. Same task, three ways in: one destination for everyone; only the scaffold changes. Pupils take the lane their do-now score pointed to (3/3 Stretch, 2/3 Core, 0–1 Support) and may move up at any time. Start the pre-teach group first: they know the words and the passage, so set them going on the task before you turn to the rest. Recall before help: every pupil tries from memory before opening a lane. The task: The Thames Barrier was first used in 1983. The Somerset Levels flooded in 2014. How many years apart are these two dates? Support — work through the steps with the group: (1) Write the later year first: 2014. Then the earlier year: 1983. (2) Count on from 1983 to 2000: that is 17 years. (3) Count on from 2000 to 2014: that is 14 more years. (4) Add the two parts: 17 + 14 = 31. Check: 1983 + 31 = 2014. Parallel worked example for Support (model it, do not give the task answer): Bangladesh flooded in 1998. The Somerset Levels flooded in 2014. How many years apart are these dates? From 1998 to 2000 is 2 years.; From 2000 to 2014 is 14 years.; 2 + 14 = 16 years. Check: 1998 + 16 = 2014.. Answer: 16 years. Core — reveal the hint only on request: Later year minus earlier year. Count on to 2000 first if it helps. Stretch — no help; when finished: The barrier was designed in the 1970s to protect London for decades. Explain why engineers might now be planning what comes after it, using the word sustainability.

## Slide 15
Same task, three ways in: Years apart
3
Routes
2
Everyone
The Thames Barrier was first used in 1983. The Somerset Levels flooded in 2014. How many years apart are these two dates?
1
Support
1 Write the later year first: 2014. Then the earlier year: 1983.
2 Count on from 1983 to 2000: that is 17 years.
3 Count on from 2000 to 2014: that is 14 more years.
4 Add the two parts: 17 + 14 = 31. Check: 1983 + 31 = 2014.
2
Core
Hint: Later year minus earlier year. Count on to 2000 first if it helps.
3
Stretch
Then: The barrier was designed in the 1970s to protect London for decades. Explain why engineers might now be planning what comes after it, using the word sustainability.
Notes: Task 2: Years apart. Same task, three ways in: one destination for everyone; only the scaffold changes. Pupils take the lane their do-now score pointed to (3/3 Stretch, 2/3 Core, 0–1 Support) and may move up at any time. Start the pre-teach group first: they know the words and the passage, so set them going on the task before you turn to the rest. Recall before help: every pupil tries from memory before opening a lane. The task: The Thames Barrier was first used in 1983. The Somerset Levels flooded in 2014. How many years apart are these two dates? Support — work through the steps with the group: (1) Write the later year first: 2014. Then the earlier year: 1983. (2) Count on from 1983 to 2000: that is 17 years. (3) Count on from 2000 to 2014: that is 14 more years. (4) Add the two parts: 17 + 14 = 31. Check: 1983 + 31 = 2014. Parallel worked example for Support (model it, do not give the task answer): Bangladesh flooded in 1998. The Somerset Levels flooded in 2014. How many years apart are these dates? From 1998 to 2000 is 2 years.; From 2000 to 2014 is 14 years.; 2 + 14 = 16 years. Check: 1998 + 16 = 2014.. Answer: 16 years. Core — reveal the hint only on request: Later year minus earlier year. Count on to 2000 first if it helps. Stretch — no help; when finished: The barrier was designed in the 1970s to protect London for decades. Explain why engineers might now be planning what comes after it, using the word sustainability.

## Slide 16
Exit ticket
Exit
Exit
Which of these is a SHORT-term way of coping with a flood?
A Putting sandbags across doorways
B Planting trees in the drainage basin
C Building the Thames Barrier
D Building a flood wall along the river
My answer:
Notes: Exit ticket — individual, silent, on a slip or mini-whiteboard. Recall before help: no notes, no lanes, no hints. Collect before pupils leave. Question: Which of these is a SHORT-term way of coping with a flood? Answer: A Putting sandbags across doorways. Sandbags are put down just before or during a flood; the others take years to build or grow. Source of this question: gate item 1 re-asked (options rotated) — this chapter has no third quick-check module. The ebook also holds task 3, "You are in charge", for homework or the next lesson's do now. Sort the slips: correct → ready to move on; incorrect → start next lesson in the pre-teach group, with the read-along and the Support lane. Same destination next time.

## Slide 17
Answers: Built to last
4
Check
Answer
A town beside a river wants protection that will last for many years. Which of these is a LONG-term flood defence?
B Building an embankment along the river
Why
Long-term defences are built or grown to last for years (embankments, walls, dams, barriers, trees). Short-term methods are used just before or during a flood (warnings, sandbags, evacuation, moving valuables).
Notes: Answers — task 1: Built to last. Reveal the answer; pupils mark their own work in a different colour, then read the "why" together. Same destination for every lane, so one answer serves the whole class. Answer: B Building an embankment along the river Why: Long-term defences are built or grown to last for years (embankments, walls, dams, barriers, trees). Short-term methods are used just before or during a flood (warnings, sandbags, evacuation, moving valuables). Ask a Support pupil to explain one step, and a Stretch pupil to share their extension.

## Slide 18
Answers: Years apart
4
Check
Answer
The Thames Barrier was first used in 1983. The Somerset Levels flooded in 2014. How many years apart are these two dates?
31 years
Why
The gap between two dates is the later year minus the earlier year: 2014 − 1983 = 31.
Notes: Answers — task 2: Years apart. Reveal the answer; pupils mark their own work in a different colour, then read the "why" together. Same destination for every lane, so one answer serves the whole class. Answer: 31 years Why: The gap between two dates is the later year minus the earlier year: 2014 − 1983 = 31. Ask a Support pupil to explain one step, and a Stretch pupil to share their extension.

## Slide 19
Answers: Exit ticket
4
Check
Answer
Which of these is a SHORT-term way of coping with a flood?
A Putting sandbags across doorways
Why
Sandbags are put down just before or during a flood; the others take years to build or grow.
Notes: Answers — exit ticket: Exit ticket. Reveal the answer; pupils mark their own work in a different colour, then read the "why" together. Same destination for every lane, so one answer serves the whole class. Answer: A Putting sandbags across doorways Why: Sandbags are put down just before or during a flood; the others take years to build or grow. Ask a Support pupil to explain one step, and a Stretch pupil to share their extension.